## Slide 1: Part #4 – CRM, Safety, Maintenance, Review

## Slide 2: Overview
Crew Resource Management (CRM)
Safety
Drone Maintenance
Review

## Slide 3: CRM
Crew Members
  Remote Pilot (you)
  Visual Observer(s)
  Person manipulating the controls
Communication
Briefing prior to mission
  Everybody understands their role

## Slide 4: Safety
Fly your drone at or below 400 feet
Keep your drone within your line of sight
Be aware of FAA Airspace Restrictions
Respect privacy
Never fly near other aircraft, especially near airports
Never fly over groups of people, public events, or stadiums full of people
Never fly near emergencies such as fires or hurricane recovery efforts
Never fly under the influence of drugs or alcohol
Hazards
  Props
  Uncontrolled Flight
  Flying over people (students)

## Slide 5: The I'M SAFE Checklist
I - Illness
  Colds, allergies, and other common illnesses can cause problems for pilots. Before flying, pilots should think about recent or current illnesses that might affect flight.
M - Medication
  With illness, it's mostly clear when a pilot should or shouldn't fly. But with illness comes medication, and all medications should be scrutinized by both the pilot and his or her doctor before taking it. Many prescription and over-the-counter medications can be dangerous for a pilot to take before flying.
S - Stress
  There are at least three kinds of stress that pilots should be aware of: Physiological, environmental and psychological stress.
  Physiological stress is stress in the physical sense. It comes from fatigue, strenuous exercise, being out of shape or changing time zones, to name a few. Unhealthy eating habits, illness, and other physical ailments are included in this category, too.
  Environmental stress comes from the immediate surroundings and includes things such as being too hot or too cold, inadequate oxygen levels or loud noises.
  Psychological stress can be more difficult to identify. This category of stress includes anxiety, social and emotional factors and mental fatigue.
A – Alcohol (and Drugs)
  There's no doubt that alcohol and flying don't mix. Alcohol abuse affects the brain, eyes, ears, motor skills and judgment, all of which are necessary components to safe flight. Alcohol makes people dizzy and sleepy which decreases reaction time.
F - Fatigue
  Pilot fatigue is a difficult problem to address completely, as fatigue affects everyone differently. Some people can function well with little sleep; others don't perform well at all without at least ten hours of sleep per night. There's no medical way to address the sleep issue with pilots -- each pilot must be responsible for knowing his or her limitations.
E - Emotion
  For some people, emotions can get in the way of behaving in a safe, productive manner. Pilots should ask themselves if they are in an emotionally stable state of mind before flying.

## Slide 6: Logs
The FAA requires logs for pilots and aircraft. The FAA may require inspection of these logs. CFR Part 61/91
Types:
  Pilot
  Flights
  Maintenance
FAA does not require logs for the UAS pilots or drones < 55 pounds explicitly
FAA Advisory Circular 107-2 (not a regulation) “Benefits of Recordkeeping. sUAS owners and operators may find recordkeeping to be beneficial. This could be done by documenting any repair, modification, overhaul, or replacement of a system component resulting from normal flight operations, and recording the time-in-service for that component at the time of the maintenance procedure. Over time, the operator should then be able to establish a reliable maintenance schedule for the sUAS and its components. Recordkeeping that includes a record of all periodic inspections, maintenance, preventative maintenance, repairs, and alterations performed on the sUAS could be retrievable from either hardcopy and/or electronic logbook format for future reference. “
CFR 107.7
  (a) A remote pilot in command, owner, or person manipulating the flight controls of a small unmanned aircraft system must –
  (3) Make available, upon request, to the Administrator any document, record, or report required to be kept under the regulations of this chapter.
CFR 107.140 Cat 4 operations requires maintenance records. Cat4 is requires FAA certification and applies primarily to operations over people.

## Slide 7: Logs
Some apps may keep operation logs.
It may be beneficial to track operational time and maintenance on your drone
It may be useful to log pilot time to document your experience.
Any logs or other data you keep on drone operations may be requested by the FAA.

## Slide 8: Operations Near Uncontrolled Airports
Commonly Class E or G
Runway directions (ex. 35/17)
Common Traffic Patterns
  Default “left traffic” (left turns)
  Right traffic may be specified (A/FD)
  Downwind (900’), Base (600’), Final (300’)
  Typically ½ to 1 mile from runway.
  Common Traffic Advisory Frequency (CTAF)
  Example radio call
Resources: Airnav.com, Airport Facility Directory (AFD)
  https://www.faa.gov/air_traffic/flight_info/aeronav/digital_products/dafd/search/
  https://www.airnav.com/
Downwind
Base
Final

## Slide 9: AFD

## Slide 10: Maintenance
Pre-flight Checklist
Li Batteries

## Slide 11: Pre-Flight Checklist
A list of items to check before flying
Develop for your drone (most don’t really have one)
Use it with your students
Some apps include an operation checklist (ex. Communications) but cannot address the physical condition.

## Slide 12: Advisory Circular 107-2 Checklist
1. Visual condition inspection of the UAS components;
2. Airframe structure (including undercarriage), all flight control surfaces, and linkages;
3. Registration markings, for proper display and legibility;
4. Moveable control surface(s), including airframe attachment point(s);
5. Servo motor(s), including attachment point(s);
6. Propulsion system, including powerplant(s), propeller(s), rotor(s), ducted fan(s), etc.;
7. Verify all systems (e.g., aircraft and control unit) have an adequate energy supply for the intended operation and are functioning properly;
8. Avionics, including control link transceiver, communication/navigation equipment, and antenna(s);
9. Calibrate UAS compass prior to any flight;
10. Control link transceiver, communication/navigation data link transceiver, and antenna(s);
11. Display panel, if used, is functioning properly;
12. Check ground support equipment, including takeoff and landing systems, for proper operation;
13. Check that control link correct functionality is established between the aircraft and the CS;
14. Check for correct movement of control surfaces using the CS;
15. Check onboard navigation and communication data links;
16. Check flight termination system, if installed;
17. Check fuel for correct type and quantity;
18. Check battery levels for the aircraft and CS;
19. Check that any equipment, such as a camera, is securely attached;
20. Verify communication with UAS and that the UAS has acquired GPS location from at least four satellites;
21. Start the UAS propellers to inspect for any imbalance or irregular operation;
22. Verify all controller operation for heading and altitude;
23. If required by flight path walk through, verify any noted obstructions that may interfere with the UAS; and
24. At a controlled low altitude, fly within range of any interference and recheck all controls and stability.

## Slide 13: Sample Checklist Items
  Build your own! Every drone is different. Common items might include:
    Battery charge
    Prop condition
    Camera free (and uncovered)
    Memory installed
    No obvious damage to airframe

## Slide 14: Review
Main difference between Part 107 and Recreational Flyer?
How high can you fly?
Give an example of a Class C or D airport.
Where can you find the area of a Class C airspace?
Where can you find the area restricted by a TFR?
How often should you inspect your drone?
If a drone weighs 2 lbs does it need to be registered?
Who has the right-of-way; drone or manned aircraft?
Your local airport has AWOS. How might you get this information?

## Slide 15: Resources
Study Guide: https://www.faa.gov/uas/resources/policy_library/#107
Advisory Circular 107-2: https://www.faa.gov/documentLibrary/media/Advisory_Circular/AC_107-2.pdf