| Obtain permission from instructor before operating this machine |  | Jointer |
| --- | --- | --- |

Safety suggestions

- Eye protection must be worn.

- Depth of cut should not exceed 1/8” (3mm.)

- Check to see that the guard is spring loaded                                                                                                                                                                                                                                and covers the cutterhead.

- Get assistance when jointing long pieces.

- Use a push stick for any stock shorter than                                                                    the fence.

- The board being jointed must exceed the minimum length specified for the machine.

Jointer

### Name    …………………..

### Class  …………………….

### Date ………………………

# Safety Quiz

| 1. | It is possible for the guard to stick and not cover the cutter. | T | F |
| --- | --- | --- | --- |
| 2. | A push stick should be used on stock shorter than the fence. | T | F |
| 3. | Eye protection is not necessary when operating the jointer. | T | F |
| 4. | The fence should be set at 90 degrees to the table. | T | F |
| 5. | Feed the wood in the direction opposing the cutterhead rotation. | T | F |
| 6. | Wood will joint smooth if the grain direction slopes down toward the operator. | T | F |
| 7. | Short stock is safe to joint. | T | F |

# Text boxes

straighten irregular

wood surfaces

Cutter

Feed

Depth scale

Power switch

Depth control

Guard

Infeed table

7.

6.

5.

3.

4.

1.

2.

Outfeed table

Fence