## Slide 1: Hilmar Ag Department Ag Welding
Anvil Project-2021

## Slide 2: Hilmar Ag Department Ag Welding
Anvil Project
Materials:
12” Railroad Track E6010 Electrodes
Equipment:
O/A Torch SMAW Welder Band Saw
Drill Press Mill Machine Cordless Drill
Angle Grinder Angle Sander/Flapper Disc
Sandblaster Pneumatic Die Grinder Flapper Wheel
Layout Tools (Hammer, Square, Center Punch, Steel Rule, SoapStone, Sharpie, Bent Wire, Number & Letter Stamps)

## Slide 3: Hilmar Ag Department Ag Welding
Anvil Project
1. Cut a 12” section of railroad track using the bandsaw (Fig. 1). Make sure the track is flat on the bed of the band saw (Fig. 2). Your piece should look like the picture below (Fig. 3).
(Fig. 2)
(Fig. 3)
(Fig. 1)
Instructions:

## Slide 4: Hilmar Ag Department Ag Welding
Anvil Project
Weigh your section of track and enter the weight on your worksheet.
(Fig. 4)
(Fig. 4)
Instructions:

## Slide 5: Hilmar Ag Department Ag Welding
Anvil Project
Instructions:
(Fig. 5)
Stamp your ID# on the bottom of your track, in the center, towards one end (This will be the back of the anvil). Make sure it is readable! You may need to use the hand grinder with a sanding disk to clean the spot before you stamp the numbers to see them better. (Fig. 5)

## Slide 6: Hilmar Ag Department Ag Welding
Anvil Project
Instructions:
(Fig. 6)
Take a picture of yourself holding your track and show it to the instructor.
Later tonight, upload it to your AET as your weekly picture. Be sure to add a caption. (This will be worth 20 Points).

## Slide 7: Hilmar Ag Department Ag Welding
Anvil Project
Instructions:
(Fig. 7)
Next, cut 2-½” off of the front end of your track (opposite the end with the number stamped on it) with the band saw (Fig 7). Your piece should look like (Fig. 8). (Put this piece in your locker RIGHT NOW!)
(Fig. 8)

## Slide 8: Hilmar Ag Department Ag Welding
Anvil Project
Instructions:
(Fig. 11)
From the same end you just cut (front end), measure another 2-1/2” (Fig. 9) and make a cut with the band saw that stops at the base of the track (Fig. 10 & 11). When the saw blade reaches the base, lift the saw (while it is still running), close the hydraulic valve, and then turn the saw off.
(Fig. 10)
(Fig. 9)

## Slide 9: Hilmar Ag Department Ag Welding
Anvil Project
Instructions:
(Fig. 13)
Use the Oxy-Acetylene Torch to make a cut from the end of the track to the band saw cut (Fig. 12), parallel to the base. You should now have a cut piece like the one shown in (Fig. 13). Put this piece in your locker after you have cooled it off.
(Fig. 12)

## Slide 10: Hilmar Ag Department Ag Welding
Anvil Project
Equipment: Angle Grinder
By changing the disc on the Angle Grinder, it can be used to remove metal and create different finishes. Here are the 3 different discs you will use on this project:
Flapper Disc
Sanding Disc
Grinder Disc

## Slide 11: Hilmar Ag Department Ag Welding
Anvil Project
Instructions:
(Fig. 15)
Use the angle grinder with a grinder disc to smooth off the cut you just made (Fig. 14). Then finish it with a sanding disc. Your anvil should now look like (Fig. 15).
(Fig. 14)

## Slide 12: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Machining the top of the anvil
With the instructor’s help, set up your anvil on the milling machine as shown in (Fig. 16). Make enough passes so that the top of the anvil is smooth (flat) and square (2 complete passes should do it).
(Fig. 16)

## Slide 13: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Layout Holes
(Fig. 17)
Use layout tools to mark where the holes will be drilled in the base of the anvil. Use the measurements shown in the diagram (Fig. 17) below to mark the holes.
See (Fig. 18-21) in the next slide for examples for marking the location of the holes.

## Slide 14: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Layout Holes
(Fig. 19)
(Fig. 18 & 19) below shows how to use the tape measure to mark the location of the holes. (Fig. 20) shows using the center punch to line up on the mark and then the result (Fig. 21) after striking the punch with a ball peen hammer.
(Fig. 18)
(Fig. 20)
(Fig. 21)

## Slide 15: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Drilling Holes
(Fig. 22) shows using the drill press to drill the 4 holes in the base. Make sure the instructor helps you set this up.
You will use a ¼” bit to drill pilot holes first, then use a 13/32”drill bit to enlarge the holes.
(Fig. 22)

## Slide 16: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Layout Anvil Horn
Measure 3” from the front end of the anvil (Fig. 23) and make a mark along both edges of the track. Using a piece of bent wire lined up with the 3” mark on the edge to the center of the front of the track (Fig. 24), make a soap stone mark to layout the top of the anvil horn. Flip the wire over to make a mark on the other side (Fig. 25).
(Fig. 23)
(Fig. 24)
(Fig. 25)

## Slide 17: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Layout Anvil Horn – Part 2
On the side of the track, hand draw the relief cutout using soapstone as shown (Fig. 26). The depth of the cutout should be 3” deep.
(Fig. 26)
3”

## Slide 18: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Anvil Horn Cutout
You will use the oxy-acetylene torch to cut out the anvil horn. Start by making the curved relief cut (Fig 28), and then the 2 cuts on top of the anvil (Fig. 27). Use a chipping hammer to remove the slag from the O/A cuts. Now your anvil should look like (Fig. 29).
(Fig. 27)
(Fig. 29)
(Fig. 28)

## Slide 19: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Trimming the Front Base
Use the band saw to trim 1-1/4” off the front of the base (Fig. 40).
(Fig. 40)

## Slide 20: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Anvil Horn Shaping
Use a 5” angle grinder to rough shape the anvil horn (Fig. 30). Check with the instructor as you progress and when given the OK, switch to a 4” grinder with a sanding disc and smooth out the grinder marks. Your anvil should now look like (Fig. 31 & 32).
(Fig. 31)
(Fig. 30)
(Fig. 32)

## Slide 21: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Tacking Rear Platform
For this step you will need the 2-1/2” piece you cut off the track back in Step 5. Position the piece upside-down on the cut-out section on the rear of the anvil. Use a vice-grip C-clamp and a square to help to position the piece correctly and square with the rest of the anvil (Fig. 33 & 33.5). When you are satisfied that everything is positioned correctly, tack it in place using E6010 rods (Fig. 34 & 35).
(Fig. 33)
(Fig. 34)
(Fig. 35)
(Fig. 33.5)

## Slide 22: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Welding Rear Platform
Weld the pieces together all around (Fig. 36). You will have to make multiple passes to fill in the spaces and gaps (Fig. 37). Be sure to chip the slag and brush the welds between passes.
(Fig. 36)
(Fig. 37)

## Slide 23: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Rear Platform Clean-up
Use the angle grinder to smooth out as much of the welds as you can (Fig. 38 & 39). Some of the weld will be in hard to reach areas for the angle grinder. The pneumatic die grinder or a flapper wheel on a cordless drill may help.
(Fig. 39)
(Fig. 38)

## Slide 24: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Shaping & Finishing
Use the angle grinder with a sanding disc (Fig. to smooth out all of your grinder marks. Then use the angle grinder with a flapper wheel (Fig. 42) to polish the bottom of the horn and the top of the anvil. Next you will use the cordless drill with a flapper wheel attachment (Fig. 43) with the correct size wheel to fit the curve under the horn (Fig. 44).
(Fig. 41)
(Fig. 42)
(Fig. 43)
(Fig. 44)

## Slide 25: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Shaping & Finishing – Part 2
Your anvil should look like the anvil in the pictures below (Fig. 45-46).
(Fig. 45)
(Fig. 46)

## Slide 26: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Sandblasting
With the instructor’s help, use the sandblaster to thoroughly clean your anvil. It should look like the anvil in the pictures below (Fig. 47-49).
(Fig. 47)
(Fig. 48)
(Fig. 49)

## Slide 27: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Final Weight
Weigh your anvil again and record your weight on your worksheet.
(Fig. 50)

## Slide 28: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Finishing
The next step is to put a finish on the anvil. Start by taping off the top of the anvil (Fig. 51). Then trim the tape as shown in figures 52-53.
(Fig. 52)
(Fig. 51)
(Fig. 53)

## Slide 29: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Finishing
Set up a place to paint making sure you cover the floor or table from overspray (Fig 54). Lay the anvil on it’s side and paint the bottom and the side and ends (Fig. 55-56). Be careful to put on a glossy coat but not so much that the paint runs (Fig 56).
(Fig. 54)
(Fig. 55)
(Fig. 56)

## Slide 30: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Finishing
Once the paint in step 24 has dried to the touch, tip the anvil up on its base (Fig 57) and paint the remaining side (Fig 58).
(Fig. 58)
(Fig. 57)

## Slide 31: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Finishing
Remove the tape on the top of the anvil. It should now look like Fig 59. Next, sand the anvil tops to remove unwanted paint, and to obtain the desired smoothness. Use the grinder with a flapper wheel or the drill with a flapper wheel (Fig 60-61).
(Fig. 60)
(Fig. 59)
(Fig. 61)

## Slide 32: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Finishing
Your anvil should look something like the one pictured below (Fig 62-64). Your anvil project is now complete and you can turn it in to be graded. Answer the questions on the next slides.
(Fig. 63)
(Fig. 62)
(Fig. 64)

## Slide 33: Hilmar Ag Department Ag Welding
Anvil Project
Instructions: Questions
What is the difference in weight of your anvil between the initial weight in step 2 and step 22? (10 pts)
Which steps in the construction of your anvil contributed to any weight loss of the anvil? (10 pts)
Which steps would have added weight to the anvil? (10 pts)
Using the “Railroad-Track-Components-Section” handout, under the “Tee Rail Data Diagram section on page 1, determine the nominal weight per yard of the rail track used to make your anvil. List the dimensions of yout track here: (25 pts)
HT -
BW -
HW -
W -
Weight per yard: