## Slide 1: Part #2 – Airspace and Charts

## Slide 2: Airspace
A – Above 18,000’
B – Large Airports (SF, LA, SD)
C – Regional Airports (Fresno)
D – Part time tower (Modesto)
E – “everywhere” (most uncontrolled airports)
  Surface, 700’, 1400’ ceilings
G – “good” unrestricted

## Slide 3: Sectional Maps

## Slide 4: Class B

## Slide 5: Class C

## Slide 6: Class D

## Slide 7: Uncontrolled

## Slide 8: Airport /Facilities Directory (AFD)

## Slide 9: Google Map

## Slide 10: Class D Example

## Slide 11: Class D Example

## Slide 12: Class D Ceilings

## Slide 13: Special Airspace
Military Operations Areas (MOA)
  Typically, over unpopulated areas for military use.
  See published altitudes on charts
Temporary Flight Restrictions (TFR)
  Fires
  Special Events (Superbowl)
  Presidential Visits
  Not on Charts, See B4Ufly

## Slide 14: MOA

## Slide 15: TFR

## Slide 16: NOTAMS (notice to airmen)
NOTAM : 1/0412
FDC 1/0412 ZLA CA..AIRSPACE TULE INDIAN RESERVATION..TEMPORARY FLIGHT RESTRICTIONS WI AN AREA DEFINED AS 360857N1184604W (TTE025018.8) TO 360231N1184823W (TTE038013.0) TO 355400N1184626W (TTE078012.1) TO 355407N1182806W (TTE075026.9) TO 360028N1182642W (TTE063028.6) TO 360920N1182818W (TTE045030.4) TO POINT OF ORIGIN SFC-13000FT. TO PROVIDE A SAFE ENVIRONMENT FOR FIRE FIGHTING AVIATION OPS. PURSUANT TO 14 CFR SECTION 91.137(A)(2) TEMPORARY FLIGHT RESTRICTIONS ARE IN EFFECT. SEQUOIA NATIONAL FOREST TEL 559-781-5780 OR FREQ 119.0750/WINDY FIRE IS IN CHARGE OF THE OPS. LOS ANGELES /ZLA/ ARTCC TEL 661-265-8205 IS THE FAA CDN FACILITY. EFFECTIVE 2109181700 UTC UNTIL 2110310900 UTC. 2109181700-2110310900EST

## Slide 17: Practical Lessons
Be aware of where manned aircraft fly
  Airports (private too)
  Traffic patterns
  Hospitals (helipads)
Sky divers (ex. Lodi, Brentwood, Woodland, Lincoln)
Crop Dusters!
Don’t fly in Class B, C, D surface area without authorization.
Use tools
  VFR Charts
  Google Maps
  Be4UFly
  TFR

## Slide 18: B4UFly

## Slide 19: No Drone Zone Areas
Restricted Airspace: The FAA prohibits drone flight over certain areas of airspace.
Local Restrictions:
  In some locations, drone takeoffs and landings are restricted by state, local, territorial, or tribal government agencies. The FAA has provided No Drone Zone signage that can be used by these governments to identify areas where there are local flight restrictions.
  It is important to note, these No Drone Zones only restrict taking off or landing and do not restrict flight in the airspace above the identified area.
The FAA may use the term "No Drone Zone" to identify an area where there is a TFR. Examples include, major sporting events, presidential movements, or in security sensitive areas designated by federal agencies.

## Slide 20: Drone Sightings
Wallace, R. J., Vance, S. M., Loffi, J. M., Jacob, J., Dunlap, J. C., Mitchell, T. A., Thomas, R., & Whyte, S. R. (2019). Cleared to Land: Pilot Visual Detection of Small Unmanned Aircraft During Final Approach. International Journal of Aviation, Aeronautics, and Aerospace, 6(5). https://doi.org/10.15394/ijaaa.2019.1421

## Slide 21: Drone Sightings
2018 Pilot sighting near airports (final approach)
Wallace, R. J., Vance, S. M., Loffi, J. M., Jacob, J., Dunlap, J. C., Mitchell, T. A., Thomas, R., & Whyte, S. R. (2019). Cleared to Land: Pilot Visual Detection of Small Unmanned Aircraft During Final Approach. International Journal of Aviation, Aeronautics, and Aerospace, 6(5). https://doi.org/10.15394/ijaaa.2019.1421

## Slide 22: Resources
VFR Charts: https://vfrmap.com/
B4Ufly: https://www.faa.gov/uas/recreational_fliers/where_can_i_fly/b4ufly/
TFR: https://tfr.faa.gov/tfr_map_ims/html/
Notams: https://www.notams.faa.gov/dinsQueryWeb/
Airspace Authorization: https://www.faa.gov/uas/programs_partnerships/data_exchange/
  UAS Facility Maps: https://faa.maps.arcgis.com/apps/webappviewer/index.html?id=9c2e4406710048e19806ebf6a06754ad
Airnav (Airport info): http://www.airnav.com
A/FD: https://www.faa.gov/air_traffic/flight_info/aeronav/digital_products/dafd/search/advanced/
Pilot’s Handbook of Aeronautical Knowledge (Chapter 15): https://www.faa.gov/regulations_policies/handbooks_manuals/aviation/phak/media/pilot_handbook.pdf