## Slide 1: Machinery Skills
Lesson 2
Tractor Safety

## Slide 2: Importance of Safety
Annually, 300 to 400 tractor-related deaths occur on U.S. farms. Over 50 percent of tractor-related deaths are caused by tractor roll-overs. A roll bar or roll-over protective (ROPS) structure and seat belt usage could have prevented all of these deaths.
Other fatalities include falls, run-overs, crushes and PTO entanglement.

## Slide 3: Types of Tractor Injury-Incidents
There are several types of tractor mishaps that result in injury. Common mishaps are:
  by-pass starting
  front-end loader incidents
  rearward tractor rollovers
  sideways tractor rollovers
  falls from tractors
  tractor runovers
  caught-between crushing
  PTO stub shaft entanglements

## Slide 4: Tractor Accidents Are Costly

## Slide 5: Tractor Operator Responsibilities
There are eight primary responsibilities the safe tractor operator must meet whenever the tractor is used. They are:
  conducts proper maintenance
  conducts pre-operation checks
  avoids injury-incident situations
  maintains safety features
  uses tractor as intended
  refuels safely
  starts and stops safely
  adjusts the tractor for safety

## Slide 6: Safe Operation
Read and understand the Operator's Manual(s) before operating the equipment.
Keep your equipment in good condition.
Never start an engine in a closed shed or garage.
Always keep your PTO properly shielded.

## Slide 7: Rules of Tractor Safety
Use ROPS and seat belt whenever and wherever applicable.
Do not wear the seat belt when the ROPS is folded.

## Slide 8: Safe Operation
Use special caution on slopes, slow down for all turns and stay off the highway whenever possible.
Keep your hitches low and always on the drawbar. Otherwise, your tractor might flip over backwards.
Keep wheels spread wide whenever possible

## Slide 9: Safe Operation
Never refuel while the engine is running or hot.
Always fuel your tractor outside and store your fuel outside.
Check the Work Area. Know in advance where hidden ditches, large rocks, stumps or any other debris is located.

## Slide 10: Safe Operation
Never Pop the clutch or practice unsafe maneuvers.
Never hitch to the axle or other high point.
Never attach a post or log to the rear wheels when the tractor is stuck in the mud.
Disengage the power take-off when it's not in use.

## Slide 11: Safe Operation
Outfit your equipment with a first aid kit, a small tool kit for minor repairs, and a fire extinguisher.
Make it a firm, unbreakable, no-exceptions rule: NO RIDERS!
Keep safety labels clean and free from obstructing material.

## Slide 12: Safe Operation
Dress Properly. Well-fitted, belted clothing is a must.
Don't jump off the tractor
Use the steps and handholds, face towards the tractor, and watch your step.
Steps should be cleaned regularly and kept free of dirt, grease and oil.

## Slide 13: Safe Operation
When you shut down your tractor:
  R. Put the PTO lever in neutral and lower attachments to the ground.
  S. Always shut off engine, set the park brake(s) and remove key.
  T. Whenever possible, park on level ground.

## Slide 14: Transport Safety
Use an SMV (Slow Moving Vehicle) sign, proper clearance flags, lights and warning signals
Be sure the brake pedals are locked together and properly adjusted to assure straight-line stops.
Prepare Your Attachments. Make sure they are secure, properly mounted. Carry them in the transport position.

## Slide 15: Transport Safety
Slow down, pull over and let the normal traffic pass you.
Control Your Speed. A tractor is designed for easy maneuverability at low speeds, not high speeds.
Slow Down on Turns or Curves.
Have the tractor in the same gear going downhill as you would to go up, in order to use engine compression for braking.

## Slide 16: Transport Safety
Never, ever, coast downhill.
Know Your Stopping Distance. Always leave enough room to stop.
Never use the differential lock while in transport. The tractor will tend to continue in a straight line when you are attempting to turn.

## Slide 17: Tractor Training Program
Fair Labor Standards Act of 1938 (FLSA) as amended: Covers employment in Hazardous Agriculture Occupations

## Slide 18: Tractor Training Program
Age 16 minimum for hazardous employment operating a tractor over 20 PTO horsepower or connecting or disconnecting an implement or any of its parts to and from a tractor.
Age 16 minimum for operating other listed hazardous farm equipment
Minors 14 or 15 years old who hold certificates of completion of either the tractor operation or machine operation training program offered by Vocational Agriculture Teachers or Extension Service may work in the occupations for which they have been trained.