## Slide 1: Machinery Skills
Lesson 4
Machinery Pre-Check Inspections

## Slide 2: What is a Pre-Check Inspection
Warm up Questions -
Recall what you know about pre-check inspection
Why is the step valuable to conduct?
What is a Pre-Check Inspection?
The initial inspection of important components listed in the manual before the operator begins to use the tractor or implement.

## Slide 3: The Daily Pre-Check
Completed before each drive.
Check before starting:
A. Engine Oil
B. Hydraulic/Transmission Oil
C. Coolant
D. Tire Inflation – visually or with gauge when available
E. Fuel
  1. Diesel or Gas
  2. Look for signs of contamination
F. Walk around – look for missing shields, and parts, worn parts, oil leaks, etc.
G. Condition of Seatbelt (if tractor has ROPS)
H. KNOW how to operate (manual, instruction)

## Slide 4: After Operator Turns on Tractor
Inspect the following before operation;
Test brakes
Test steering
Test hydraulic response
Check oil pressure using gauge on display panel

## Slide 5: Once Tractor is in Use
Use safety equipment
Water temperature
Oil Pressure
Fuel Pressure (diesel)
Fuel Level (Diesel is important)
Hydraulic response
Changes in operation
3 L’s – Look, Listen, Live

## Slide 6: Example Pre-Check Inspection Sheet

## Slide 7: Build a Culture of Safety
Safe Operation
  1. Saves money in lost work time
  2. Reduced maintenance
  3. Reduced worker’s compensation rates
Safety Training is required by law
Safety is everybody’s responsibility

## Slide 8: Lets Practice Our Pre Check Skills
Please look at the following three pictures and identify issues that you would report to the farm manager.