## Slide 1: Machinery Skills
Lesson 5
Tractor Hitching Operations

## Slide 2: Question
How are Implements connected to a tractor?
What does PTO Stand for?
What do you know about a Quick Hitch?

## Slide 3: Drawbars
Single point of connection
THE ONLY CONNECTION FOR TOWING
Adjustable in and out
  Shorten for implements with long tongues
Fixed or Swinging
  Fixed for road travel
  Swinging for towing heavy implements
Use inverted position for PTO clearance

## Slide 4: Drawbars
Fixed Drawbar
  Does not move side to side
  Made of solid steel
  Numerous holes to place ball hitch based on implement needs
  Typically mounted low on the tractor

## Slide 5: Drawbar Leverage
Proper Attachment | Improper Attachment
Proper pull angle reduces flips. Use designated draw bar. | Connecting too high on tractor creates a dangerous pivot point

## Slide 6: Three Point Hitches
Sized by Category
  Cat. I. – small tractors 15-35 HP
  Cat II. 30-75 HP
  Cat III. 60-168
  Cat. IV. 135-300
  Category specifies the dimensions of the “A” frame and pin size

## Slide 7: Three Point Hitches cont…
Hitch Components
  Draft Links
  Top or Center Link
  Lift links, one is adjustable
  Rocker shaft arms
  Sway Chains

## Slide 8: Three Point Hitches cont…
3 points are identified by red arrows
  Top arrow –
    Top Link
  Lower left arrow –
    left draft link
  Lower right arrow –
    right draft link
  Hooking up implement to Three point hitch - video

## Slide 9: Three Point Hitch Converted to Quick Hitch
Allows for a quick and easily attach and release of three-point implements without leaving your tractor seat
Three-point quick hitches are made of heavy duty steel construction
Locks in implement using spring loaded levers uses letting you attach drag harrows, lawnmower rakes, box blades, augers and other implements

## Slide 10: Power Take Off (PTO)
Used to provide power to an implement
Two speed are common 540 and 1000 RPM
Shafts are three sizes with two RPM rates
  1 3/8” (540)
  1 3/8” (1000)
  1 ¾” (1000)
PTO Safety
  Guard in place
  Securely attached to PTO Shaft
  Drawbar clearance Universals move freely