## Slide 1: Machinery Skills
Lesson 6
Power Systems

## Slide 2: Major Systems
Power systems required to operate modern tractors
  Engine
  Power Train
  Hydraulic
  Electrical

## Slide 3: Engine
Power source of the equipment
  Provides for all systems
  Engine – Power Train- PTO- Wheels- Hydraulics
Types
  Gasoline
  LPG
  Diesel

## Slide 4: Gas Vs. Diesel
Method of supplying and igniting fuel
Higher compression ratios in diesels
  8:1-Gas
  16:1- Diesel
Generally, more rugged design of diesels
Grade and type of fuel

## Slide 5: Supplying Fuel
Gas Engines
  Air and Fuel are premixed prior to compression stroke of engine
  Can be carbureted or fuel injected
Diesel
  No premixing of fuel and air
  Fuel is injected under high pressure the beginning of the power stroke
  Air is compressed prior to fuel injected

## Slide 6: Compression Ratio
Compares the volume of air in the cylinder before compression with volume of air after compression.
Higher compression in diesel is to
  increase air temperature and
  better thermal efficiency.

## Slide 7: Design
Diesels must be built sturdier to withstand greater forces of combustion.
  1. Diesels have a more powerful power stroke because of the efficiency of the engine.
4 Strokes:
  Intake
  Compression
  Power
  Exhaust

## Slide 8: Fuel
Fuel energy is measured in British Thermal Units (BTU’s)
  Diesel has higher BTU count per gallon
  Diesel: 139,000 BTU’s per gallon
  Gasoline: 124,000 BTU’s per gallon
Diesel fuel injection systems are more expensive than a gasoline fuel system

## Slide 9: Engine Systems
Required systems for engine operation
  Fuel
  Intake/Exhaust
  Lubrication
  Cooling
  Electrical
  Governing

## Slide 10: Fuel Systems
Gasoline
  Tank
  Pump
  Filter
  Carburetor/injector

## Slide 11: Fuel Systems
Diesel
  Tank
  Transfer Pump
  Filters
  Injection Pump
  Injection Nozzle
Notes: This is a simple fuel system on a diesel, considered to be a “pump and pipe” system.

## Slide 12: Intake
Air Cleaner
Intake Manifold
Turbo Charger (if used)
Intake Valve
Intercooler (If used)

## Slide 13: Exhaust
Exhaust Valve
Exhaust Manifold
Muffler
Turbo Charger (if used)

## Slide 14: Lubrication System
Reduces friction, dissipates engine heat and helps clean parts
Reservoir
Pump
Filter
Regulating Valve

## Slide 15: Cooling System
Prevents overheating of engine and regulates it’s temperature
50/50 mix of coolant/water
Radiator
Pressure cap
Fan
Pump
Thermostat

## Slide 16: Electrical System
3 Circuits
  1. Charging
    Battery, Voltage Regulator, Alternator
  2. Starting
    Switch
    Starter
  3. Ignition
    CPU
    Depends if diesel or gas

## Slide 17: Governing System
Keeps engine speed at constant level
Prevents engine over speeding
Get engine to match load at all times
Types
  Mechanical
  Hydraulic
  Electrical

## Slide 18: Power Trains
Essentially the transmission that transmits power from engine to the wheels & pto
4 jobs of Power Train
  Connects and disconnects power
  Selects speed
  Provides a means to reverse
  Equalizes power to the drive wheels for turning

## Slide 19: Mechanical-Drive
5 Basic Components
  Clutch
  Transmission
  Differential
  Final Drive
  Drive Wheels

## Slide 20: Clutch
A. 3 Types
  Disk (mechanical or hydraulic)
  Overrruning
  Cone
Notes: Clutch Connects and Disconnects power from the engine to the transmission

## Slide 21: D/C Electricity
D/C (Direct Current) is the most common polarity of electricity in agriculture machines.
Charging, starting, ignition systems and computer modules all require DC electricity.
In new equipment, electricity is used throughout the entire machine.

## Slide 22: Electricity
A. Electricity
  Movement of free electrons in a conductor
  Initiated by mechanical or chemical means
  Must have a complete circuit

## Slide 23: Terms to know
A. Terms for Measurement
  Voltage
    Pressure or push behind the electron flow
  Amperes
    Amount or volume of these electrons
  Watts
    Measure of quantity of work overtime direct ratio to Kw/H.P.
  Resistance
    Ohms

## Slide 24
Multi-Meter Information
A, Multi-Meters are a tool that can be used to diagnose and Electrical system.
B. The illustration is a typical multi-meter

## Slide 25
D/C Circuits

## Slide 26: Series and Parallel Circuits
A. In series circuits, current can only take one path.
B. The amount of current is the same at all points in a series circuit.

## Slide 27: Series and Parallel Circuits
C. In parallel circuits the current can take more than one path.
D. Because there are multiple branches, the current is not the same at all points in a parallel circuit.

## Slide 28: Conclusion
Tractors have multiple systems that produce power or energy
Each system is integral to the agriculture machinery industry
Hydraulics are continued on unit 06.1