## Slide 1: Machinery Skills
Lesson 6.1
Hydraulic Basics

## Slide 2: Introduction
In production agriculture, hydraulics have become an integral component to most aspects of modern machinery.
Below is a foundation list of where hydraulics are used on modern tractors and equipment:
  Steering
  Hitches
  Transmissions
  Clutches
  Implement control
  Brakes
  Remotes

## Slide 3
Basic System
Notes: This is an illustration of simple hydraulic system. The pump supplies pressurized fluid to the cylinder to increase work.

## Slide 4: Terms/Acronyms
PSI-Pressure of hydraulic fluid
  Measured in Pounds per Square Inch
GPM-Flow of hydraulic fluid
  2. Gallons per Minute
Horsepower-Unit of measurement
  3. Rate of which work is done
Cylinder-Component that converts hydraulic pressure and flow into work or mechanic force.
Pump-Component the creates flow of hydraulic fluid.
Motor-Component the converts hydraulic flow into mechanic motion or torque.

## Slide 5: Hydraulic Systems
2 Common systems of a hydraulic system:
  Open Center
    Constant flow of fluid through the center of the control valve.
  Closed Center
    Pump can slow or stop hydraulic flow based on needs of equipment.

## Slide 6
Hydraulic Spool Valves

## Slide 7
Comparing Hydraulic Systems-Open Center

## Slide 8
Comparing Hydraulic Systems-Closed Center

## Slide 9: Pump vs. Motor
Notes: Common example of a gear pump and gear motor. Biggest difference is the exit on the pump is small than the entrance allowing the pump create pressure by restricting the flow.

## Slide 10
Basic Principles:
  Liquids can fit to shape of its container.
  Liquids cannot be compressed like air
  Liquids will transfer energy
Hydraulic Principles

## Slide 11
Hydraulic cylinders
  Utilize Pressure and Flow to extend and retract.
  Pressure is responsible for pushing or exerting a force or torque.
  Flow is responsible for making the cylinder move.
  There are many types of cylinders, the most common found on agriculture equipment are single-acting and double-active cylinders.
Cylinders

## Slide 12
Cylinders

## Slide 13
Cylinders
Notes: Illustration of the differences between a double acting and single acting cylinder.

## Slide 14
Schematic:
  Map of hydraulic system using symbols
  Allows for a technician to see how the hydraulic flows through a system
Hydraulic Schematics
Notes: Illustration of a simple hydraulic schematic

## Slide 15
  Understanding hydraulics takes time
  Technicians need to have a vast understanding of a hydraulic system
  Hydraulics are a power system of all agriculture tractors
Conclusion