## Slide 1: Machinery Skills
Lesson 7.1
Tillage Principles

## Slide 2: What are tillage Implements?
Warm up questions –
When you read the word tillage, what comes to mind?
What do implements have to do with tillage?

## Slide 3: Definitions
Tillage - Mechanical soil stirring actions carried on for the purpose of growing crops
  1. There are several Tillage Categories . . .
Primary tillage
  Initial, deeper tillage after crop harvest to begin preparation of seedbed and root zones for next cropping cycle.
  2. Performed to at least a depth of 6 inches and most normally one or two feet or more.

## Slide 4: Definitions
Secondary Tillage
  Shallow tillage for final, refined seedbed preparation prior to planting.
  Normally performed to no more than 3 to 4 inches in depth.
  Performed after primary tillage
Cultivation
  Shallow post planting tillage to loosen soil and /or eradicate unwanted vegetation.

## Slide 5: Primary Tillage Objectives
Management of crop residues
Weed control
Improvement of soil tilth (physical characteristics of soil)
Opens up soil for deeper root growth
  1. Refer to picture of corn roots

## Slide 6: Secondary Tillage Objectives
Soil aeration
Incorporation of fertilizers
Moisture management
Insect control
  1. Bury crop residue to eliminate host site for pests.

## Slide 7: Cultivation Objectives
Temperature control for seed germination
Provide good seed/soil contact.
Prepare soil surface for other operations.
  1. Build furrows and beds.
  2. Smooth surface for harvest operations.
Erosion control

## Slide 8: Tillage Operation and Implements

## Slide 9: Question
Which implement would be used for primary tillage?
  Offset Stubble Disc
                B. Rotary Cultivator
  C. Ring Roller
Notes: Answer is “A”

## Slide 10: Primary Tillage
Cutting through the soil.
Shattering the soil.
Inversion of soil.
Mixing of soil.
Pulverization of soil clods.
Examples of primary tillage Implements
  1. Moldboard plows
  2. Subsoilers and chisels
  3. Offset disk harrows
  4. Rotary tillers
Implements require high horsepower tractors

## Slide 11: Secondary Tillage
Additional soil pulverization.
Leveling the soil.
Firming the soil.
Killing weeds.
Examples of secondary tillage Implements
  1. Disk harrows
  2. Spring and spike tooth harrows
  3. Landplanes
  4. Listers (bed forming)

## Slide 12: Cultivating
Killing weeds.
Loosening and aerating the soil for better water penetrations and root aeration
Moving soil to form beds.
Examples of cultivating tillage implements.
  1. Power incorporators.
  2. Cultivating knives and sweeps.
  3. Spring tooth harrow.

## Slide 13: Typical Fall Tillage Sequence

## Slide 14: Question
Which tillage system involves the most machine horse power? Why?
  Primary Tillage
  Secondary Tillage
  Cultivation
Notes: Answer is A, due to its large amount of soil movement.