## Slide 1: Machinery Skills
Lesson 8.1
Sprayers and Calibration

## Slide 2: Question
In a sprayer like the one pictured the Gallons per Acre applied is effected by the:
  Ground speed
  Nozzle size
  Boom width
  Pressure
  All of the above

## Slide 3: Common Types of Sprayers
Boom
  1. Used for row crops
  2. Self-propelled
  3. Towed
  4. Tractor mounted (3 point or other attachment)
  5. Implement mounted
Air-blast
  1. Orchards and vineyards
  2. Varying designs for direction of the spray
Aerial (fixed wing and helicopter)
  1. High volume

## Slide 4: Basic Sprayer Components
Tank
Screen Filter
Pump
Hoses
Pressure Regulator
Pressure Gauge
Valves
Boom
Nozzles

## Slide 5: Tank
Holds the mixed (chemicals & water)
Plastic or Stainless Steel
Large opening for easy mixing
May include mixing jets
Bottom outlet to pump
Inlet for return flow

## Slide 6: Sprayer Components
Strainer & Screens
  1. Prevents wear to the pump
  2. Prevents nozzle clogging
  3. Mounted on tank or inline
  4. Nozzle strainers are mounted on each nozzle
Pressure relief valves
  1. Adjustable spring loaded valve

## Slide 7: Valves
Used to control flow to specific sections of nozzles
Manual ball valves or electrical operated valves- Like your automatic sprinkler system in your yard

## Slide 8: Nozzles
Distributes the spray
Controls droplet size, decrease as pressure increases
Controls flow as a function of pressure
Picture below depicts spray patterns that are nozzle specific

## Slide 9: Boom Assembly
Nozzle Assembly
  1. Holds nozzle secure as it emits spray
Breakaway Hinge
  1. Allows the section of boom to bend to reduce further damage if it hits something like a pole or tree.
Boom Arms
  1. Steel structure that supports hoses and nozzles

## Slide 10: Plumbing Design

## Slide 11: Spray Nozzles
Spray pattern effect of worn tips
  1. Left – New tips: Coverage Variance 6%
  2. Center – Worn tips: Coverage Variance 35%
  3. Right – Damaged tips: Coverage Variance 57%

## Slide 12: Spray Nozzles
Spray Coverage

## Slide 13: Nozzle Selection
Select a nozzle that applies 20 GPA at 5MPH with a medium droplet size.
What pressure?
  1. See Tee Jet table on next slide

## Slide 14: Nozzle Selection

## Slide 15: Question
Doubling the nozzle pressure will:
  Double the nozzle flow
  Increase the nozzle flow
  Decrease the nozzle flow
  Not affect the nozzle flow
  Both A & B

## Slide 16: Relationship of Flow and Pressure
For example a nozzle with an output of .1 GPM @ 10 psi will output .2 GPM @ 40 psi

## Slide 17: Calibration
Sprayers need to be calibrated to insure correct amount of chemical or product is applied.
Active ingredient vs. spray quantity
  1. Prescription is given in active ingredient
  2. Ex. gallons/ac or pounds/acre or ounces/acre

## Slide 18: Calibration
Factors
  1. Spray Rate (gallon/min)
  2. Sprayer Width
  3. Speed
Width is fixed
Rate is controlled by nozzle & pressure and can be considered fixed for a given application
Speed controlled by operator

## Slide 19: Needed Calibration Formulas

## Slide 20: Active Ingredient vs. Spray Amount
Sprayer is calibrated by total spray amount (ex. 20 gal/acre
Chemical is added to water at a prescribed rate per acre.
  1. Ex. 32 oz of chemical per acre applied in 25 GPA of spray

## Slide 21: Sample Problems
Tank contains 500 gallons to be applied at 35 GPA. How much chemical is added at 40 oz per Acre?
Sprayer will operate at 4 MPH determine the GPM if the sprayer width is 50’

## Slide 22: Sample Problems
A boom sprayer has a 300 gallon tank and is calibrated at 25 gallons per acre. A 12 acre field is to be sprayed with X, Y and Z pesticides. How much of each pesticide would be used to make one tank full of mix? The pesticide application rates from the labels are:
X = 1 pint/acre Y = 1.5 pounds/acre Z = 2 ounces/acre