## Slide 1: Machinery Skills
Lesson 9.1
Equipment and Implements
Planters and Seeders Identification

## Slide 2: Planters/Seeders
Planters and seeders are common in production agriculture
The units must meter seed output and place seed precisely for proper germination
Can be use for vegetable crops, forage and other types of plants for human and/or animal consumption.

## Slide 3: Vacuum Vegetable Planter
Notes: This unit uses vacuum to hold seeds against a seed plate. The seed plates are responsible for metering the seed output. A brush is used to knock the seed off the plate sending it down the seed tube.

## Slide 4: Large Seed Planter
Notes: This unit uses seed plates that can be changed out for various crops. Typically used for corn, cotton, sorghum and other plants that start as a larger seed.

## Slide 5: Drawn Air Planter
Notes: Can be used for various crops, utilizes air pressure to move seeds from a large hopper to the individual planting unit. Works well for large acreage.

## Slide 6: Small Seed Vegetable Planter
Notes: As you can see this planted has smaller hoppers than the previous planters. This planter is responsible for planting small vegetable seeds on raised beds like lettuce, broccoli and cauliflower.

## Slide 7: End Wheel Grain Drill
Notes: Drills are used for the process of solid seeding which is planting seeds across a wide area. Unlike row crop planters, the seeds planted with this unit are not spaced. The end wheels of this drill drives the metering system that supplies seeds from the hoper to the seed tubes.

## Slide 8: Press Wheel Grain Drill
Notes: Press wheel drills are like the end wheel drill except the press wheels are the driving component that works the seed metering system. The press wheels also firm the soil around the seeds as it passed through the field.

## Slide 9: Seed Broadcaster
Notes: Broadcasters can be used for seeding as well as fertilizing. Broadcasters are not as accurate as drills when seeding a field.

## Slide 10: Sled Seeder
Notes: Sled seeders use electronic devices to move seeds around a hopper and drop them down a seed tube. Used with small seed applications.

## Slide 11: Conclusion
The previous slides are examples of many types of planters/seeders/drills used in production agriculture.
This is an example of the diversity of the agriculture industry nation and worldwide.
The technology in modern equipment has allowed less farmers to feed more people.