## Slide 1: Machinery Skills
Lesson 9.3
Grain Drill Identification

## Slide 2: Introduction
Grain drills are commonly used in forage/hay production throughout the United States
This lesson will allow you to learn common parts of an end wheel grain drill

## Slide 3: Category II Three Point Hitch
Notes: There are different category sizes for 3 point hitches. This unit requires a medium horsepower tractor to pull it at the correct speed this is why it has a category II hitch size.

## Slide 4: Drive Wheel
Notes: This drill has two drive wheels which drive the seed metering devices

## Slide 5: Seed Hopper
Notes: Stores the seed above the metering devices

## Slide 6: Seeding Chart
Notes: This chart helps the operator calibrate his seeder to the specific seed they are planting.

## Slide 7: Double Disc Furrow Opener
Notes: This components opens the soil to all allow the seed to be dropped below the soil surface

## Slide 8: Slow Moving Vehicle Emblem (SMV)

## Slide 9: Jack Stand
Notes: This component allows the operator to park the drill so that it is level on the ground. It must be removed during operation

## Slide 10: Gate Adjustment Lever
Notes: This lever allows the operator to adjust the seed gate

## Slide 11: Fluted Feed Seed Monitor
Notes: This is the metering device for this drill

## Slide 12: Seed Gate
Notes: Adjustable gate used in calibrating drill, three different adjustments as shown in the pictures.

## Slide 13: Seed Tube
Notes: Transfer component, guides the seed from the hopper through the fluted wheel to the double disc furrow opener

## Slide 14: Spring Tensioner
Notes: Spring pressure is used to hold the furrow openers on the ground, this unit has an adjustment for both the top and bottom of the tensioner to increase or decrease down pressure

## Slide 15: Driven Sprocket (Red Low, Yellow High)
Notes: This sprocket is driven by the chain attached to the drive wheels. This sprocket controls the speed of the fluted wheel seed metering mechanism. The red arrow is pointing to the low speed sprocket, the yellow arrow is pointing the high speed sprocket.

## Slide 16: Conclusion
Having a basic understanding of components and parts is an integral skill that is useful when troubleshooting equipment.