## Slide 1: Estimating Fixed Costs
MEAG 120

## Slide 2: Costs
One of the most important cost influencing farming operations is owning and operating machinery.
Good management can minimize costs associated with machinery
Accurately estimating machinery costs can aid in minimizing
Estimates play an important role in decisions
  When to trade
  Which size to buy
  How much to buy

## Slide 3: Costs
Two main types of machinery costs
  Fixed costs-depending more on how long a machine is owned rather than how much it is used
  Operating costs-varying in proportion to the amount of use
Fixed Costs:
  Depreciation
  Taxes
  Shelter
  Insurance
  Interest
Operating Costs:
  Fuel
  Lubrication
  Maintenance
  Repairs
  Labor

## Slide 4: Depreciation
Loss of value of a machine due to time and use
Often largest of all costs
Reasons:
  Age-Newer machine is worth more than older machine
  Wear-More use, more wear, may keep breaking down
  Obsolescence-Major model chance or not enough capacity, value may be greatly reduced, new technology can make existing equipment obsolete.

## Slide 5: Depreciation
Calculate depreciation in different ways:
  Straight-line depreciation
  Sum-of-the-digits depreciation
  Declining-balance depreciation

## Slide 6: Straight Line Depreciation
Equal reduction of value is used each year the machine is owned
Can always be used to estimate costs over a specific time
  Provided the proper salvage value is used for age of machine
Annual Depreciation (AD)=(Price-Salvage Value)/Years own
Self propelled swather is purchased for $40,000.00 and it’s “life” is assumed to be 10 years. Assume it’s salvage value at ten years to be ten percent of new cost.
  40,000-4,000/10= $3600.00 per year

## Slide 7: Straight Line Depreciation
Not quite accurate for giving the true value
Machines depreciate much faster in the first few years than in later years
Best use is for estimating costs over the entire life of the machine
  As long as salvage value is an actual

## Slide 8: Sum-Of-The-Digits Depreciation
Accurate in estimating the true value of a machine at any age
  Annual depreciation rate decreases as machine ages
Higher depreciation rate at early years of machine
3 Steps
  Add the numbers representing the years covered by the depreciation period.
  Divide the total depreciation by the sum of the digits of the years for depreciation period.
  Proportion the depreciation in reverse of the years over which the depreciation occurs as shown by the following example.

## Slide 9: Sum-Of-The-Digits Depreciation
Apply to the same swather used previously
Cost $40,000.00, Salvage value $4,000.00 at 10 years
Total value: 40,000-4,000= 36,000
1. Sum of the digits: 10+9+8+7+6+5+4+3+2+1= 55 depreciation units
2. Depreciation per units: 36000/55= 654.545 per unit
3. Depreciate in reverse of years
  1. 10 X 645.545= 6545.45
  2. 9 X 645.545= 5890.91
  3. 8 X 645.545= 5236.36
  4. 7 X 645.545= 4518.82
  10. 1 X 6545.545= 6545.55

## Slide 10: Declining Balance
Reflects actual value of machine
Machine depreciates a different amount each year, but the same percentage of the remaining value is depreciated
“As Is” value assumes the machine must be sold on the open market without trade in or at an auction
R.V.=P x (1-r/L)y
R.V.= Remaining Value
P= Initial Price
r= Rate of depreciation
L= Life, years
y= Age at which remaining value is determined

## Slide 11: Declining Balance
Whatever beginning value each year will be worth a fixed percentage of the value one year later
Swather example:
Price:40,000 X 20%= 8,000
32,000 X 20%= 6,400
25,600 X 20%= 5,120

## Slide 12: Declining Balance
First year correction factor
  Added in declining balance depreciation
Formula’s
  All combines, tractors and crawlers:
    R.V.=list price x .67 x .94y
  Forage Harvesters
    R.V.=list price x .67 x .90y
  All others
    R.V.=list price x .67 x .92y
  y- age of machine in years, indicates how many times the annual depreciation factor is multiplied by itself.

## Slide 13: Declining Balance
Example:
$50,000.00 tractor that is valued at 27,825 after 3 years
50,000 x .67 x .943
$27,825.00

## Slide 14: Other fixed costs
Taxes
Shelter
Insurance
Interest

## Slide 15: Fixed Costs
Taxes
  Depending on state
  Could be assessed in the same manner as property
  Some states have a sales tax
Insurance
  Typically .25 to .50 of the R.V. of the machine
Shelter
  Dependent on location
  Experts agree that equipment that is not stored under a shelter, more repairs will be needed. Machines deteriorate faster when exposed to the elements
  Typically 1-2 percent of R.V. or machine

## Slide 16: Fixed Costs
Interest
  Direct expense on borrowed capital
  Range between 8%-12%

## Slide 17: Estimating Fixed Costs
Taxes, shelter, insurance and interest can be combined in order to estimate costs. (TSII)
Dependent on your interest rate
  If you interest rate is 9% and the others add up to 4 percent
  Annual charge of 13% of the R.V. at the beginning of the year would be reasonable for fixed costs.

## Slide 18: Total fixed costs for 100K tractor
End of Year | R.V. | Depreciation | TSII | Total Cost
0 | 85,000 |  |  | 
1 | 62,980 | 22020 | 11050 | 33070
2 | 59,201 | 25799 | 19237 | 45036
3 | 55,649 | 29351 | 26934 | 56284
4 | 52,310 | 32690 | 34168 | 66858
5 | 49,172 | 35828 | 40968 | 76797
6 | 46,221 | 38779 | 47361 | 86139

## Slide 19
End of Year | Tractors/Combine | Forage Harvester | All Other
1 | 33.07% | 35.75% | 34.41%
2 | 22.52% | 24.81% | 23.68%
3 | 18.76% | 20.70% | 19.75%
4 | 16.71% | 18.33% | 17.55%
5 | 15.36% | 16.69% | 16.06%
6 | 14.36% | 15.42% | 14.93%
7 | 13.56% | 14.39% | 14.01%
8 | 12.90% | 14.39% | 13.24%
9 | 12.33% | 13.51% | 12.57%
10 | 11.82% | 12.75% | 11.98%
11 | 11.37% | 12.07% | 11.45%
12 | 10.96% | 11.46% | 10.96%
13 | 10.58% | 10.91% | 10.52%
14 | 10.23% | 9.94% | 10.11%
15 | 9.91% | 9.51% | 9.72%

## Slide 20: Example
6 year old tractor with annual use of 400 hours, originally listed for $80,000.00. What is the average cost per year for depreciation, taxes, shelter, insurance and interest after 6 years?
14.36% of list price from Table
.1436X80,000= $11,488
What is the average cost per hour?
$11,488/400= $28.72 per hour

## Slide 21: Low Annual-Use Fixed Costs
Fixed cost per hour changes according to the amount of annual use.
  Total annual fixed cost is not greatly affected by annual use
  The more time equipment is used, the lower the average fixed cost per hour of per unit of use
Self propelled combine is being considered, two possibilities: One combine lists for $130,000 and the other $100,000. There are 1,000 acres of crops to be harvested each year. What is the difference in fixed cost per acre, if planned to own the combine for 12 years. Use the table.
  .1096X130,000= $14,248 per year or $14.25 per acre
  .1096X100,000= $10,960 per year or $10.96 per acre

## Slide 22: Low Annual-Use Fixed Costs
Expanding lowers annual-use fixe costs in some situations
Add 500 acres to previous example:
  .1096X130,000= 14,248 per year or $9.50 per acre
  .1096X100,000= 10,960 per year or $7.31 per acre
Which unit would you choose?

## Slide 23: How to Reduce Fixed Costs?
Fixed costs account for 50-75% of total machinery costs
You can reduce fixed costs more easily than you can operating costs
  Have proper amount of equipment
  Longer ownership of equipment
  Buy used equipment

## Slide 24: Proper Amount of Equipment
If you have the most efficiently matched tractors to equipment, you will have substantially lower fixed costs than if you have more equipment or larger equipment.
Example:
  You own two 140 hp tractors that originally listed for $70,000.00 each. You are thinking about buying an 80 hp tractor at $42,000.00 to pull some lighter equipment. If you plan to own the equipment 8 years then you average annual cost is 12.9% of list price (Table 3).
  12.9% of list price of two 140 hp tractors is
    .129 X 2 X 70,000= $18,060.00 per year
  Add an 80 hp tractor at $42,000
    .129 X 42,000= $5,418
    30% increase in costs

## Slide 25: Used Equipment
Use table 1 to gain an idea of how much a piece of equipment is worth at a given year.
Different options in buying used equipment
  Dealer
  Auction/Sale
  Direct from another farmer
What would you expect to pay for a used $80,000.00 list price tractor that is 4 years old?
  52.31% X 80,000= $41,841
  25% increase from dealer for “Reconditioning”= $52,310.00

## Slide 26: Practice
Using straight line depreciation, what is the annual depreciation of a $100,000.00 Combine over a 10 year life if the salvage value of the equipment is 10% of original cost?
In the above question, what is the remaining value of the combine after 3 years?
What is the average annual fixed cost for a $60,000.00 tractor that is 5 years old?