## Slide 1: Fuel and Lubrication Costs
MEAG 120

## Slide 2: Fuel and Lubrication
True Operating Costs
  Fuel is directly proportional to amount of use
16-45% of total operating costs (not including labor)
Fuel and lubrication costs increase as annual use increases.
  Fuel and lubrication costs per hour remains constant, but takes higher percentage with higher annual use as Fixed cost decrease per hour.

## Slide 3: Needs/Estimation
Horsepower-hours of energy
  Amount of fuel needed per acre is proportionate to the amount of energy needed.
  Chapter 7 Table 2
Fuel types
  3 types
    Gasoline (9 Hp-HRs/Gal)
    Diesel (13 Hp-HRs/Gal)
    LPG (7.5 Hp-HRs/Gal)
Fuel Consumption
  Average Fuel Consumption for the Machine must be known

## Slide 4: Average Fuel Consumption (Yearly/Hourly)
Diesel: 0.044 gallons per hour per PTO Hp
Gasoline: 0.068 gallons per hour per PTO Hp
LPG: 0.080 gallons per hour per PTO Hp
What’s the average fuel cost for a 60 hp diesel tractor with the average fuel price at $3.75 per gallon.
  60hp X .044 = 2.64 gallons per hour
  2.64 Gallons/Hour X 3.75 gallon= $9.90/hour average fuel cost

## Slide 5: Practice
What would the average fuel cost be to operate a 100 engine hp tractor with diesel fuel costing $4.25 per gallon?
What would the average fuel cost be to operate a 50 engine hp tractor with gasoline fuel costing $4.89 per gallon?
What would the average fuel cost be to operate a 75 engine hp tractor with LPG fuel costing $4.25 per gallon?

## Slide 6: Lubrication Costs
Wide variety of lubricants used on modern equipment
  Engine Oil
  Grease
  Transmission Fluid
  Hydraulic Fluid
Multiply fuel cost by 10% to determine estimated lubrication cost.

## Slide 7: Lubrication and Fuel Cost
Keep records of fuel consumption per piece of equipment
10% factor
Fuel and Lubricant costs usually represent 20-30% of total machine costs (operating costs)
Fuel and Lubricant costs increase as annual use of equipment increases

## Slide 8: Estimating
Amount of energy needed per acre for each type of operation is nearly constant, regardless of size of the power unit of machine.
The amount of fuel used is proportional to the amount of energy in performing each field operation.
For most farming operations, a tractor will operate at 55% of its rated power during the year.

## Slide 9: Practice
What is the average hourly and annual fuel consumption for a 100 hp (PTO Rated) tractor, if it is used 450 hours a year? Also, estimate the annual fuel and lubrication costs with diesel at $3.49 per gallon.
  Hourly:
  Annual:
  Fuel Cost:
  Lubrication Cost:

## Slide 10: Practice
If fuel costs average $12.50 per hour for your tractor, how much would you expect to spend for lubricants?
Which type of tractor is most efficient in converting fuel to useful work?

## Slide 11: Practice
How much would you save in diesel fuel costs if you are pulling a planter with a rated 200 PTO hp tractor and you use half throttle and a higher gear? You are planting 1,000 acres at 10 acres per hour. Assume diesel fuel is $3.48 per gallon and full throttle fuel consumption is 6.5 gallons per acre.