## Slide 1: Improving Efficiency

## Slide 2: Intro
Ability to improve field efficiency is an important step in developing management skills.
Some lost-time factors are built into the operation
Other factors can be eliminated by good planning and management.

## Slide 3: Factors of Lost Time
Typical Factors:
  Unused capacity
  Filling procedures
  Unloading procedures
  Turning and field conditions
  Unclogging machines
  Making adjustments
  Reducing breakdowns
  Servicing machines
  Rest breaks
Changing Operators
Checking machine performance
Unmatched machine capacity
Any of these factors may contribute greatly to lost time.

## Slide 4: Factors
Unused Capacity
  Falls on how the operator uses the equipment
  Using fullest possible width
  Keeping machine adjusted
  Better planning, careful driving and correct machine adjustment can increase efficiency.
Filling Procedures
  Time-loss by up to 20% is not unusual for filling hoppers on planters
  Travel time
  Use larger hoppers, plan better ways to refill

## Slide 5: Factors
Unloading Procedures
  Have a good setup on how to unload
  Where you stop your equipment is important for the truck or shuttle to maneuver
Turning Time and Field Conditions
  Turning time is the one loss factor built into every field operation
    Can be minimized by having longer rows
    Typically 12-15% of field time
  Rough terrain, obstructions
  and ditches

## Slide 6: Factors
Unclogging Machines
  Prevent overloading
  Make sure equipment is operating properly
  Operate when conditions are right
Making adjustments
  Check over machine prior to operating in the field
  Make sure it is adjusted properly

## Slide 7: Factors
Reducing Breakdowns
  Inspect and repair machines ahead of use for the season
  Practice preventative maintenance
  Avoid rocks, holes, obstructions
  Drive cautiously
  Don’t overload equipment
  Check out strange sounds, vibrations or smells
  Make minor repairs when needed
  Periodically check equipment
  Keep all power transmitting members adjusted, aligned and lubricated
  A well running machine is a safer machine

## Slide 8: Factors
Servicing Machines
  Service before or at the end of the day
  Some maintenance like lubrication may need to happen throughout the day, this cannot be neglected
Rest Stops
  Short, but frequent rest stops are desirable
  Avoid prolonged and unnecessary stops
Changing Operators
  Try to change operators in the field

## Slide 9: Factors
Checking Performance
  Take a few minutes and spot check the machine
  Look for loose bolts, worn parts
Unmatched Capacity
  Increase capacity with each operation
    Harvest nuts with pickup machine
    Shuttle must have larger capacity
    Trailer must have larger capacity
    ETC….

## Slide 10: Summary
Better operators will help in making operation efficient

## Slide 11: Application
If a 14 foot disk overlaps an average of 20” with each pass, what is the operators field efficiency? The tractor is traveling at 6 mph.
What difference does 30 min of lost time make in a 10 hour day for a planting operation that otherwise averages 10 acres per hour?
How much longer would it take to plant 1,000 hours if 30 minutes were wasted every day? Assume a 10 hour day.