## Slide 1: Machinery Management
Introduction

## Slide 2: The Beginning
Machinery Management has increased in importance on today’s farms
  Direct Relationship to success through:
    Mixing land, labor and capital to return a profit
Machinery costs overshadow all other crop production costs
  Except land
Machinery costs account for 50 percent of total production costs
  Can be as high as $200.00 per acre or more

## Slide 3: Problems
Problems of management are varied
Each problem could be the difference between a profit or loss
Examples:
  How much machinery should be owned?
  What size equipment is needed?
  Should custom operation be used?
  How often should equipment be traded?
  Should a machine be repaired or traded?

## Slide 4: How much?
Typical farms have needs for
  Tillage
  Planting
  Harvesting
Each area has “fixed costs” which could eat up profits quickly
  Depreciation
  Taxes
  Shelter
  Insurance
  Interest

## Slide 5: How much?
Lack of equipment may mean not getting crops planted or harvested on time.
Costs associated with farming other than land:
  Machinery-50%
  Labor-11%
  Fertilizer- 10%
  Seed- 10%
  Chemicals- 6%
  Other- 13%

## Slide 6: What size?
Larger vs Smaller?
  Larger equipment lowers labor costs
    Can complete big acreage in a hurry
    Unless there is high annual use, the equipment can cost more than labor
    Need to own 10-12 years if not used regularly
  Smaller tractors cost less per hour
    High annual use, may be ready to trade in 6-8 years
    Less capacity
    Can take longer to get the job done

## Slide 7: Size cont.
Combination of expected performance and expected costs
Both capacity and capital costs increase with size
  At the same time, performance improves, especially in critical operations.
Delays in planting or harvesting can take a toll on yields
  These losses are called “Timeliness Losses”
    Timeliness Loss- crop yields and quality are affected by the dates of planting and harvesting. Too soon or too late can have an effect on your profit margin.

## Slide 8: Custom?
In some situations it may be practical or less expensive to use custom operations.
  Specialty crop on small acreage
  Using custom may be cheaper than purchasing equipment needed
  Custom operations may have a larger capacity
  Cost benefit needs to be weighed between ownership.

## Slide 9: Trade in?
When do you trade in?
  Frequent may lead to reduced cost of maintenance but may be more expensive per acre to run
  “Pride of Ownership”- having the latest, greatest, newest…etc.
  May need to trade in due to neglect of equipment
  Average costs may be higher to trade in frequently
  With good maintenance, average tractors will last 8-10 years (produces lowest cost per hour)
  Older machines have more downtime, typically

## Slide 10: 4 Elements of Trading in:
Average cost per unit of use
Cost to trade compared to making repairs
Reliability of machine
Net effect on profit of total farming operation

## Slide 11: Repaired or Traded?
Can be a difficult decision.
Age of current machine and reliability of machine are important factors
  Constant breakdowns or down time may indicate its ready to be traded
  Having reliable equipment is the best way to hold down costs of production

## Slide 12: Operating Costs
Labor
Fuel
Lubricants
Repairs
Operating costs are typically lower than Fixed or Overhead costs
  Typically something you can control
Reducing operation costs by 10-15% can save up to $5.00 per acre
Improperly matching equipment can increase operating costs by up to 20%.