## Slide 1: Measuring Capacity

## Slide 2: Capacity of a machine
Rate of performance
  Depending on type, performance or capacity will be measured by:
    Acres per hour
    Tons per hour
    Hundred weight per hour
As a manager it is important to understand how to estimate capacities they plan to buy for future use.
  Be able to complete field work on time
  Avoid added expenses

## Slide 3: Measuring methods
Acres per hour is the most common measure of machine capacity
3 possible measurers
  Field capacity (Acre/Hour)
  Material Capacity (Hundredweight/hour)
  Throughput capacity (lbs,Tons/hour)

## Slide 4: Field Capacity
Most commonly used measurement of machine capacity
  ac/hr = feet/min x 60 min/1 hr x implement width feet x 1 acre/43560 sq ft
  ac/hr = speed, mph x implement width, ft
8.25
3 Factors
  Speed
  Width
  Efficiency

## Slide 5: Field Capacity
Speed-Average rate of travel expressed in MPH or Feet per minute
Width- Distance in feet across processing portion of the machine
Efficiency- Ratio of effective field capacity to its theoretical field capacity
  Ratio of how much time is spent working and total time in field
Effective field capacity
  ac/hr = total acres
  Total hours

## Slide 6: Material capacity
Once known as bushels per hour, now counted as hundredweight(cwt) per hour
Measure of material such as silage or grain, harvested by a machine
Not completely accurate as it measures the amount of grain or forage harvested, not the total amount or material passing through the machine.
  Example: Wheat, corn, oats…etc

## Slide 7: Material Capacity
(tons / hr) = cwt/hr x 100 lbs/1 cwt x 1 ton/2000 lbs
(lbs/Hr) = pounds/1 min X 60 min/1hr x 1 cwt/100 lbs
Use of weight as a unit of work instead of an area

## Slide 8: Throughput capacity
Total amount of material per hour
Lbs/min x 60 min/1hour

## Slide 9: Capacities
All examples are “theoretical” in nature
Effective capacity brings in efficiency
In theory, you can estimate how long or how much you can produce which can help in determining your needs.

## Slide 10: Practice
A tractor pulling a 15 ft disk at 4.5 mph, what is the theoretical field capacity (TFC)?

## Slide 11: Practice
A cotton picker traveling at 300 ft/min, in one minute, 150 lbs of cotton pass through the head of the picker. What is the material capacity of the cotton picker in tons/acre? Or tons/hour?

## Slide 12: Practice
A combine harvesting wheat traveling at 350 ft/min, in 1 minute, 1000 lbs of material in passed through the header of the machine. Of that 1000 lbs, 350 lbs is discharged out the back of the machine. What is the material capacity of the machine? The combine head is 18’ wide, what is the field capacity of the machine? What is the throughput capacity of the machine?

## Slide 13: Best operating speed
Modern units work best at a given speed
  Example- Modern tillage units work best at 5-7 mph
    Going too slow will not allow tool to break up soil
    Going too fast might throw the soil too far or break the equipment
  Power may be wasted in draft at increased speeds

## Slide 14: speed
Power requirements may limit speed
  Heavy crop, or trash may require you to reduce your speed
Some applications may require a precise speed
  Spraying
Do a speed check prior to operating in the field
  Speedometers may not be accurate
    Tire size
    Field conditions

## Slide 15: Speed
(mph) = ft/min x 60 min/ hr x 1 mile/5280 ft
(Mph) = distance, ft
time, min X 88
88 ft in 1 min = 1mph
Swather with a 18’ head that take 334 seconds to go 2800 ft, what is the mph?

## Slide 16: Speed
With an increase in speed, greater emphasis is needed on safety
  Operator
  Equipment

## Slide 17: Practice
A tractor pulling a disk 1500 feet in 1 min 45 seconds, what is the mph?

## Slide 18: Field Capacity & efficiency
Theoretical field capacity- maximum possible capacity at a given speed.
  Assuming machine is using full width
Effective field capacity- accurate check of the area actually covered over a period of time
  Total acres/total hours
Efficiency
  EFC/TFC X 100

## Slide 19: Practice
If the tfc of a 14 foot self-propelled windrower us 7 acres per hour, and it cuts 63.7 acres in 13 hours, with is the field efficiency?
What is the effective field capacity of a 6-row, 30 inch header equipped corn combine traveling 3.33 mph, assuming A FIELD EFFICENCY OF 60%?
What is the field efficiency of a 16 ft chisel plow traveling 4.5 mph if it averages 65 acres in a 10 hr day?