## Slide 1: Power Ratings and Matching

## Slide 2: Soil Resistance
See chart in hand out
How much drawbar horsepower is required to pull a 16’ chisel plow with medium soil type?

## Slide 3: Determining Size
Power measurements
  Brake-Engine HP without alterations
  PTO-Power measured at the PTO
  Drawbar-Pulling power-varies based on soil surface, type of hitch
  Hydraulic-Power created by the hydraulic system

## Slide 4: Converting Power
Factor of 87
  87% can be used to convert either engine or drawbar power to an equivalent PTO rating
  Example
    Tractor with an engine hp of 350 would have 87% of 350 or 304.5 as the equivalent PTO hp rating.
    A tractor rated with 200 drawbar hp would be approximately 87% of rated PTO power. Dividing 200 by .87 gives us a PTO hp of 230.

## Slide 5: Matching
When matching a tractor and implement, three important factors must be considered:
  Tractor must not be overloaded
  Implement must be pulled at the proper speed or optimum performance can not be achieved
  Soil conditions and their effects must be considered.
    With a given tractor, there is a set amount of power available. This available power is used for:
      Moving the tractor over the ground
      Pulling the implement over the ground
      Powering the implement for useful work

## Slide 6: Matching
2 Factors to prevent overloading
  Match for high speeds to reduce loading and were on the tractor power train.
  Ballast the tractor so you will have 10%-15% wheel slip for good tractive conditions
Overloading with too large an implement and using excessive ballast is a major reason for early power train failures.
The softer or looser the soil conditions, the greater the amount of power that will be consumed because of greater rolling resistance.
  Reduces available useable drawbar power.

## Slide 7: Example
How large a disc harrow could be pulled with a MFWD (FWAD) tractor rated at 140 PTO Hp, assume firm soil conditions.
  Use Table 2
  65 or 70 percent of 140 PTO Hp= 91Hp or 98 Hp.
  Assume from Table 1, medium soil, 340 lbs of draft per foot or 4.5 Hp per foot of width.
    91 Hp/4.5= 20.2 Ft
    98 Hp/4.5= 21.78 ft

## Slide 8: Example
If the implement is known, required tractor size can be determined
  How large a 4 wheel drive tractor would be needed to pull a 9 shank V-Ripper at 4.25 mph? Assume draft of 1900 lbs per shank.
  Table 1- 21.5 usable Hp per shank
    21.5X9= 193.5 hp
  Assuming firm traction conditions, table 2 indicates 66% of rated PTO Hp as being usable.
  193.5 is 66 Percent of the required PTO Hp
  193.5/.66= 293 rated PTO Hp
  The tractor would need to be 293 PTO Hp or 337 Engine Hp (293/.87)

## Slide 9: Slippage
Proper slippage is important to have the most efficient use of tractor power.
Too much wastes energy reduces available power
Overballasted wheel slippage will be low, but rolling resistance will be high, again wasting power
  Can overload the powertrain
No. of turns, loaded-No. of turns, no load/No. of turns, no load X100

## Slide 10: Slippage
Example:
  Tractor pulling a disc, when the disc is in the ground there is 10 revolutions, when the disc is lifted traveling the same distance the tires have 9 revolutions. What is the slippage percentage?

## Slide 11: Critical Work Periods
Do not base machinery selection on average weather conditions, base it on years of poorest weather conditions.
Example: You have 170 working hours on years with poorest weather conditions.
Don’t count on keeping the tractor running continuously, some experts say at best 85% of available working time is spent in the field.
.85X170=144 hours

## Slide 12: Practice
To chisel plow 1,000 acres in 144 hours, ca capacity of 6.94 acres per hour would be needed. Assuming 82% field efficiency and a speed of 5.5 mph, what would be the would be the size of chisel plow needed? What engine PTO would be needed?
What drawbar Hp is required to pull a disk with a total draft of 4,000 pounds at 5 mph?
How fast can you pull a 10,000 pound load with a tractor that has 100 useable drawbar Hp?
A tractor using 60 drawbar hp is pulling an 18’ disc at 5 mph, what is the draft per foot of width?