## Slide 1: Production Agriculture
Systems and Equipment

## Slide 2: Equipment Needs
Based on application
Must be the right size for the work to be done
Proper capacity match to related equipment
Tractors and implements are categorized by horsepower rating of tractor
  Drawbar Horsepower
  PTO Horsepower
  Engine Horsepower
  Hydraulic Horsepower

## Slide 3: 3 pt Hitch Sizes
Category | Upper Pin | Lower Link | Hitch Spacing | Drawbar Power
0 | 5/8” | 5/8” | 20” | <20hp
1 | ¾” | 7/8” | 26” | 20-45hp
2 | 1” | 1 1/8” | 32” | 40-100hp
3 | 1 ¼” | 1 7/16” | 38” | 80-225hp
4 | 1 ¾” | 2” | 46” | 135-300hp

## Slide 4: Drawbar Hitch Sizes
Category | Drawbar | Pin Diameter
0 | 38 | 1”
1 | 64 | 1 ¼”
2 | 154 | 1 ¼”
3 | 248 | 1 ½”
4 | 402 | 2”
5 | 671 | 2 ¾”

## Slide 5: Horsepower
33,000 lbs, 1 ft, 1 min
Most new equipment is rated by engine horsepower
Loss of power by approximately 15% from engine to pto or drawbar
Hydraulic horsepower is psi x gpm / 1714

## Slide 6: Torque
Twisting or rotational force
The work being done
Torque is the least at the engine and greatest at tires
Reduction of speed from engine to final drive

## Slide 7: Power Transfer
Engine to clutch or torque converter, to transmission, to differential to final drive
Engines have a maximum power and torque rating
  Power is dependent on size, design, speed and the load

## Slide 8: Power within Agriculture
Many farms and ranches are dependent on the power or torque created by machinery
Technology in machinery has made some jobs easier and more efficient
Reduction in labor, increase in labor cost have forced many aspects of the industry to evolve to be more economical
Figuring out what you need is key to the success of your operation

## Slide 9: Field Crops
High horsepower requirement
  Tractors 150 hp +
  Tillage equipment
    Primary and Secondary
    Listers, disk etc
  Chemical Application
  Forage harvesting
    Swather, Baler…etc $$$
  Grain/Silage harvesting equipment
    Combine, chopper…etc $$$$

## Slide 10: Veg Crops
Medium horsepower requirement
  Tractors 110-150 hp
  Tillage equipment
    Primary, Secondary, Minimum
  Drip tape installation
  Plastic mulch installation
  Seedbed prep
  Cultivation
  Chemical application
  Harvesting

## Slide 11: Orchard Equipment
Medium horsepower requirement
  Tractors 80-100 hp
    Low profile
  Tillage equipment
    Primary for pre planting (ripping..etc)
    Secondary and Minimum
  Weed Control
  Land prep for harvest
  Air blast sprayer
  Harvesting equipment $$$$
  Pruning equipment
  Shredders

## Slide 12: Vineyard
Medium horsepower requirement
  Tractors 80-100 hp
  Tillage
    Set up for specific row spacing (Secondary)
  Land prep
  Chemical application
    Aerofan or AirBlast
  Wine grape, raisin grape harvesting equipment
  Pruning equipment
  Shredders

## Slide 13: Livestock
Medium horsepower requirement
  Tractors 80 hp
  Feed trailers/wagons
  Livestock trailers
  Scrapers
  Feed prep equipment
  Material handling
  Pasture maintenance equipment
  Chemical application

## Slide 14: Spraying
Tractors
Spray Cabs (does not protect completely)
Three point lift sprayers
Pull type
Self propelled
Airblast or aerofan
Electrostatic
Safety equipment
Shields
Booms/Broadcast

## Slide 15: Applications
Tillage
  Preparation of an effective seed bed
    Oxygenation of seedbed
    Provide intimate seed/soil contact
    Incorporate crop residue
  Enhance infiltration rate
  Moisture control and aeration
  Weed control
  Reduce chemical residue

## Slide 16: Tillage
Types
  Primary
    Move large amounts of soil
    Break up hard pan
  Secondary
    Move medium amounts of soil
    Clean trash
    Setup seedbeds

## Slide 17: Tillage
Types:
  Reduced
    Less soil manipulation
    Increase in chemical use
  Conservation
    Reduce soil loss
    Control Erosion
    Incorporate crop residue
    Chemical weed control

## Slide 18: Tillage
Types:
  Non-Inversion
    Fracture the soil
    Leaves surface rough
  Inversion
    Inverts the soil to bury residue
    Little or no residue left on surface

## Slide 19: Conservation Management Practices
CMP’s
  Allow operation to have a plan in managing soil
  Determines what is needed for operation
  Conservation has become key in soil health on today’s farms
  Rotating crops, rotating tillage..etc has shown benefits in managing land resources
  Prevention of soil erosion is the foundation of CMP’s

## Slide 20: Planting
Dependent on crop planted
  Row crop
    Vegetables, fruit, etc..
  Field Crop
    Grains, hay, silage, etc…
  Permanent Crop
    Trees/vines, bushes, etc…

## Slide 21: Planting
What to plant?
How to manage?
How to harvest?
All questions you should ask before start of growing season
Tractor requirements/needs have to be figured out prior to decision

## Slide 22: Harvest
Tractor requirement
CMP’s pre-harvest
  What is needed to be done to the soil prior to harvest