## Slide 1: Tread Widths, Wheels and Tires

## Slide 2: Tires radial vs bias ply
Bias-ply
Cheaper
Stiff strong durable tire
More stable (hillsides)
Increased sidewall puncture resistance
Radial
Increase field efficiency
Increase fuel efficiency
Tire footprint 20% larger
Higher drawbar pull
Less field compaction

## Slide 3: Rear tire designs
Standard or general purpose cleat
  Standard “V” tread best compromise for traction, flotation, and tread life
High cleat
  Maximum tractions in mud
  Tread wears rapidly
Nondirectional
  Great for sandy soils and slopes
  Smoother ride and better for hard surfaced roads
Industrial lug
  Wider tread increase wear resistance
  Typically used during earthmoving operations

## Slide 4: Front tire designs
Single rib
  Used in loose soil, helps with steering control
Double and triple rib
  Give good steering control with less compaction
Flotation
  Less compaction with more difficult steering
Rice Tread
  Great for wet conditions
Angle bar
  Similar to rear tires used with MFWD

## Slide 5: Wheels
Made from cast iron or steel
  Most have inner cast iron disks with a steel rim
Most wheels are dish shaped

## Slide 6: Rear wheel adjustment-Reversing the wheels
The inner part of the wheel is placed away from the centerline of the rim
When wheels are interchanged the dish is facing in or out
Wheel disk could be permanently attached
  Two tread options
Wheel disk could be fastened
  Allows for more tread options

## Slide 7: Rear wheel adjustment-Positioning Rim Clamps
Wheel is attached using clamps
Can have up to four tread settings

## Slide 8: Rear wheel adjustment-Rack and Pinion Adjustment
Wheels are adjusted in place
Cap screws lock the hub of the wheel
Once loosened the pinion will rotate and adjust the wheel spacing

## Slide 9: Rear wheel adjustment-Positioning Wheel Hub
Hub is made from two pieces
Creates a clamping force on the axle
Wheel is adjusted to desired position
Hub is clamped down

## Slide 10: Rear wheel adjustment-Power Adjustment
Has a spiral guide rail that covers the whole rim
  Each rail extends from one side of the rim to the other
One guide rail has holes for the stop fitting which control tread width

## Slide 11: Front Wheel Tread Adjustment
If the rear tires can adjust and the tractor has a wide front axle those tires must have the ability to adjust
The axle either has
  Smaller round tube inside larger tube
  Extension axles that are bolted on
In either design the tie rods need to adjusted

## Slide 12: Front Wheel Configuration
Wide front axle
  Stable, smooth ride
  Larger turning radius
Mechanical Front Wheel Drive axle
  Better operation on tough terrain and reduce wheel slip
Narrow front axle-dual wheels
  Best for most row spacings no adjustment needed
Narrow front axle-single wheel
  Used with narrow spaced rows or beds

## Slide 13: Dual Rear tires
Advantages:
Reduces slippage
Greater stability
Less compaction more flotation
Smoother ride
Used with higher power requirements
Ability to use in adverse weather conditions
Disadvantages:
Axles may be overstressed
If work is light no advantage other than less compaction
More difficult to turn
If not needed a lot the cost may be too great

## Slide 14: Tractor Weight- Wheel weighting
Weight can be iron or liquid
  Liquid stiffens the tires
Liquid is a mixture of water and calcium chloride to prevent freezing
Liquid fills 75% of the tire
Typically not removable
Cast iron weights are added to the wheel
Depending on size these are easily removed
Weight can be adjusted for each job

## Slide 15: Tractor Weight- Frame weighting
Easily adjusted for different operations
Typically weights have a handle for easy installation and removal
Weights should be removed when maximum traction isn't needed
  Soil compaction is increased
  More fuel consumption