## Slide 1: Surveying Skills
Lesson 2
Surveying Tools Quiz

## Slide 2: Chaining Pins – Used to mark points of distance on the ground

## Slide 3: Fiberglass Tape – Common lengths are 50, 100, and 300’. Not as accurate as a chain.

## Slide 4: Chain – A steel tape used for accurate measurement. The unit “chain” is 66 feet.

## Slide 5: Measuring Wheel – Use to measure longer distances. More accurate than pacing, but less accurate than a tape.

## Slide 6: Level – A simple telescope that can measure horizontal angles.

## Slide 7: Transit – A telescope that can measure horizontal and vertical angles.
Notes: Note how telescope can be rotated up and down to measure vertical angles.

## Slide 8: Total Station – A telescope that can measure horizontal and vertical angles as well as distance. Uses a reflector instead of a rod. Software does the trigonometric computations to compute the position of the target.
Notes: Look for these in use around highway construction.

## Slide 9: Laser Level and Receiver - The level generates a level laser beam. The receiver is attached to a rod and moved up and down to intercept the beam.

## Slide 10: Laser Level and Receiver - The level generates a level laser beam. The receiver is attached to a rod and moved up and down to intercept the beam.

## Slide 11: Rod Target – The target us used when measuring long distances where the rod cannot be read through the telescope. The target is moved up and down on the rod by the rod man.

## Slide 12: Rod Level – Attached to the rod and used to hold it plumb
Notes: These are useful is training the rodman to hold the rod plumb.

## Slide 13: Builder’s Rod - A rod marked in feet and inches.

## Slide 14: Philadelphia Rod – A rod marked in feet and hundredths of feet

## Slide 15: Direct Elevation Rod – The rod has a movable tape that is adjustable, so the readings reflect the change in elevation.
Notes: Commonly used with laser levels to measure field slope.

## Slide 16: Tripod – Supports the instrument.
Notes: Note that different instruments use tripods with different heads.

## Slide 17: Plumb Bob – Used to locate an instrument above a point or to measure plumb (up and down) in building.

## Slide 18: Hand Level - A handheld telescope with a level bubble. Useful for estimating slope.

## Slide 19: Surveyor's Tape -- Plastic tape used to mark stakes.