## Slide 1: Surveying Skills
Lesson 2
Surveying Tools

## Slide 2: Tools Used in Surveying
Distance Measuring Tools
  Tapes
  Measuring Wheels
  Surveyor’s Chain
Level and Angle Measuring Tools
  Survey Instruments
    Levels – measure vertical changes and horizontal angles
    Transits – Measure vertical and horizontal angles
    Total Stations – measure angles and distance

## Slide 3: Tools
  Elevation Rods
    Used to measure vertical distances
    Philadelphia – Measures in 100th of feet
    Builder’s Rod – Measures in feet and inches.
    Direct Elevation - Has movable measuring tape and directly reads elevation in 100th of feet
  Laser Levels
    Rotating laser set level or to a slope
    Uses a special target (laser detector)

## Slide 4: Other Tools
Plumb Bob
Surveyor’s Tape
Hand Level
Tripod - supports the instrument
Rod Targets - attaches to the rod for easier reading.

## Slide 5: Chaining Pins – Used to mark points of distance on the ground

## Slide 6: Fiberglass Tape – Common lengths are 50, 100, and 300’. Not as accurate as a chain.

## Slide 7: Chain – A steel tape used for accurate measurement. The unit “chain” is 66 feet.

## Slide 8: Measuring Wheel – Use to measure longer distances. More accurate than pacing, but less accurate than a tape.

## Slide 9: Level – A simple telescope that can measure horizontal angles.

## Slide 10: Transit – A telescope that can measure horizontal and vertical angles.
Notes: Note how telescope can be rotated up and down to measure vertical angles.

## Slide 11: Total Station – A telescope that can measure horizontal and vertical angles as well as distance. Uses a reflector instead of a rod. Software does the trigonometric computations to compute the position of the target.
Notes: Look for these in use around highway construction.

## Slide 12: Laser Level and Receiver - The level generates a level laser beam. The receiver is attached to a rod and moved up and down to intercept the beam.

## Slide 13: RTK GPS – A highly accurate device that uses the Global Positioning System (GPS) for surveying and precision agriculture
Notes: Note GPS base station with antenna (left) and rover (right)

## Slide 14: Rod Target – The target us used when measuring long distances where the rod cannot be read through the telescope. The target is moved up and down on the rod by the rod man.

## Slide 15: Rod Level – Attached to the rod and used to hold it plumb
Notes: These are useful is training the rodman to hold the rod plumb.

## Slide 16: Builder’s Rod - A rod marked in feet and inches.

## Slide 17: Philadelphia Rod – A rod marked in feet and hundredths of feet

## Slide 18: Direct Elevation Rod – The rod has a movable tape that is adjustable, so the readings reflect the change in elevation.
Notes: Commonly used with laser levels to measure field slope.

## Slide 19: Tripod – Supports the instrument.
Notes: Note that different instruments use tripods with different heads.

## Slide 20: Plumb Bob – Used to locate an instrument above a point or to measure plumb (up and down) in building.

## Slide 21: Hand Level - A handheld telescope with a level bubble. Useful for estimating slope.

## Slide 22: Surveyor's Tape -- Plastic tape used to mark stakes.

## Slide 23: Review

## Slide 24: What is the name of this tool?
Notes: Chaining Pin

## Slide 25: What is the name of this tool?
Notes: Fiberglass Tape

## Slide 26: What tool is used to measure longer distances. More accurate than pacing, but less accurate than a tape.
Notes: Measuring Wheel

## Slide 27: What tool is a simple telescope that can measure horizontal angles?
Notes: A level

## Slide 28: What is a telescope that can measure horizontal and vertical angles called?.
Notes: A transit

## Slide 29: What are the names of these two tools?
Notes: Laser Level and Receiver. NOTE: If you have your own unit use pictures of your unit.

## Slide 30: What type of rod is marked in feet and inches?
Notes: Builders Rod

## Slide 31: What type of rod is marked in feet and hundredths of feet?
Notes: Philadelphia Rod

## Slide 32: What tool supports the instrument?
Notes: Tripod