## Slide 1: Surveying Skills
Lesson 3
Pacing

## Slide 2: Pacing
A pace is the distance (in feet) from the heel of one foot to the point where the heel of the other foot hits the ground.
Pacing is useful for measuring distances where higher precision is not needed for example estimating the length of piping needed to plumb a new building.
No tools required!
Distances can be measured by pacing when no greater than 2% accuracy (2 feet in 100 feet) is required.

## Slide 3: Determining Your Pace
Pace can be determined by the following technique:
Accurately measure off a 100-foot distance.
At a normal walk, count the number of steps it takes to cover the 100 feet. Record the steps.
Repeat three more times recording the steps. The number of steps should be similar, but may be different. For example you might get 39, 41, 40, 41 steps. This is OK.

## Slide 4: Calculation of Your Pace
Average the number of steps from your 4 walks. For example: (34 + 36 + 35 + 35) ÷ 34 = 35 steps
To determine an individual’s pace, divide the average number of steps into 100 feet. For example: 100 feet ÷ 35 steps = 2.9 feet/step

## Slide 5: Using Pacing
When using pace to determine distances, it is best to determine pace under the same conditions that the distance is to be measured.
  For example, pace will vary if measurements are taken uphill or downhill, in wet or muddy conditions, in tall or short vegetation, or in loose or firm soil.
Pace out the unknown distance counting your steps.
Compute the distance (hint: phone calculator). Steps x Feet/step = feet walked
For example, you need to quickly determine how much pipe is needed to connect a new shop to an existing water system. You pace the distance and count 125 steps.
125 steps x 2.9 feet/step = 363 feet
Note: Pipe is sold in 20’ lengths so your estimate is 19 pieces.
Notes: Walk students through the math with some additional examples