## Slide 1: Surveying Skills
Lesson 4
Right Angle Layout

## Slide 2: Uses
Layout a row at right angles from a road.
Layout of forms or foundations
Land Area Measurement

## Slide 3: Laying Out a Right Angle
Right angles (90o angle) can easily be created with a tape using the 3-4-5 method
Used for forming concrete and similar tasks
Use any multiple of 3,4, and 5
Limited by tape length
Longer measurements are more accurate
3,15,30
4,20,40
5,25,50

## Slide 4: Method
Layout one of the legs of the right triangle (ex. Leg AB) the “4” distance and mark both ends. Note: Use chaining pins, stakes, or mark on existing forms, etc.
Using two tapes (easier), measure the other leg the “3”(AC) distance and hypotenuse (sloping side) the “5” (CB) distance from the two marked points locating the third point.
A
B
C

## Slide 5: Checking for Square
Rectangular (and square) forms or foundations can be checked for square by measuring the diagonals.
Opposite sides must be the same dimension
If the shape is square then the diagonals will be equal.
Diagonals are Equal
Diagonals are Not Equal

## Slide 6: Forms are Not Square
Top of form needs to be moved in the direction of the arrow
Notes: Explain how moving the form in the direction indicated will shorten up the longer diagional. NOTE: Form (or project) must have equal opposite sides for this to work.

## Slide 7: Forms are Square