## Slide 1: Surveying Skills
Lesson 5
Determining Field Area
Notes: This is foundation for other skills.

## Slide 2: Using a tape to determine field area
Field area can be determined by using common formulas for shape areas.
  Square or rectangle. Length x Width
  Right triangle: ½ Height x Width
Calculate the area of the field in square feet first.
Then divide the area of the field in square feet by 43,560 square feet / acre to determine the area of the field in acres.

## Slide 3: Measuring the distances
Measure the length and width with a tape. This is easily done with two people, a long tape, and chaining pins.
  The lead person stretches the tape full length and marks the point with a chaining pin.
  The measurement is recorded.
  Then the tape is advanced to the chaining pin. And the process is repeated.
  If desired the trailing person can recover the chaining pin after the measurement is complete.
A measuring wheel can be used but will not be as accurate.
Pacing can be used for an estimate.

## Slide 4: Square and Rectangular Fields
The length and width are measured.
Calculate the area in square feet.
For example: 1250 ft. x 800 ft. = 1,000,000 square feet.
Divide the area to determine acres by 43560 sq. ft. / acre

## Slide 5: Triangular Fields
The width (base) and length (height) are measured.
Calculate the area in square feet.
For example: 500 ft. x 900 ft. ÷ 2 = 225,000 square feet.
Divide the area to determine acres by 43560 sq. ft. / acre
Use only for “right” triangles

## Slide 6: Circular Fields
Fields irrigated by center pivots commonly are circular.
The radius (pivot point) or diameter are measured.
Calculate the area in square feet.
For example using the radius: 3.14 x (563 ft.)2 = 995,283 sq. ft.
Divide the area to determine acres by 43560 sq. ft. / acre
For ½ circle simply divide by 2.

## Slide 7: Irregularly-shaped fields
Make an accurate (scale) drawing of the field.
Break the field down into recognizable shapes and compute the area of each part.
Add all of the areas of the parts of the field to get the total area of the whole field.

## Slide 8: Example
Break into a rectangle and triangle.
740 ft. x 1310 ft. = 1964683 sq. ft.
740 ft. x 300 ft. / 2 = 111000 sq. ft.
1965683 + 111000 = 2075683 sq. ft.
2,075,683 / 43,560 = 47.65 Acres

## Slide 9: Formulas
Use the following formulas to determine the area of common geometric-shaped fields:
  Square or rectangular fields: Area = (width)(length) Where, width = width of the field in feet length = length of the field in feet
Notes: Use the formulas to practice. Make up a few examples and work together with the students.

## Slide 10: Formulas (Cont.)
  Triangular fields: Area = (1/2)(base)(height) Where, base = length of the base of the triangular field in feet height = perpendicular height to the base of the triangular field in feet

## Slide 11: Formulas (Cont.)
  Circular fields (center pivot irrigation): Area = (3.1417)(d )/4 Where, d = diameter of the field in feet