## Slide 1: Surveying Skills
Lesson 6
Level Setup
Notes: This is foundation for other skills.

## Slide 2: Setting the Tripod
Leg Clamp
Head
Open the tripod and place legs about 2.5 to 3 feet apart.
Press the points firmly in the ground. If on a hard surface us a stand.
Loosen the leg clamps.
Adjust the legs to bring the head to a comfortable reading height and level. Lock the leg clamps.
Notes: This works well with an actual instrument and tripod.

## Slide 3: Attaching the level
Attach the level to the tripod using the screw.
Note that the instrument may be adjusted laterally to position a plumb bob over a BM (Bench Mark) if desired.

## Slide 4: Auto Levels and Laser Levels
Auto Level and Laser Levels are self-leveling as long as the tripod is within a few degrees of level.
No leveling screws are needed.
Laser levels typically will not rotate until they are level.
Some auto levels have a bubble level to indicate that they are mounted close enough to level for the auto level to function.

## Slide 5: 3 Screw Levels

## Slide 6: Adjusting 3 Screw Levels
Mount the instrument on the tripod and line up the telescope vial in position (a) as shown.
Then grasp screws A & B so that both thumbs are moving in opposite directions, either toward each other or away from each other.
Note that the bubble moves in the same direction as your left thumb.
Keep about half the foot screws length engaged.
When the bubble is centered in position (a), turn the instrument and observe the vial in position (b).
Now center the bubble in position (b) using only screw C.
Check to see that the instrument is level by rotating to random positions. The level bubble should remain centered. If not repeat the procedure.

## Slide 7: 4 Screw Levels (Dumpy Levels)

## Slide 8: Adjusting 4 Screw Levels
Mount the instrument on the tripod and line up the telescope in line with two opposite screws (a).
Adjust the screws that are aligned to the telescope. Grasp screws the two screws so that both thumbs are moving in opposite directions, either toward each other or away from each other.
Note that the bubble moves in the same direction as your left thumb. Adjust until the bubble is centered.
Rotate the telescope 90 degrees so it aligns with the other two screws (b). Repeat steps 2 and 3.
Rotate the telescope back to the original position and adjust as necessary.
Check to see that the instrument is level by rotating to random positions. The level bubble should remain centered. If not repeat the procedure.

## Slide 9: Aiming and Focusing
Rotate the instrument by hand to aim the telescope to the far object or a rod.
Rotate the focusing knob until the object can be observed clearly.
Always focus the telescope before attempting to read the rod.

## Slide 10: Cross Hairs
Cross Hairs

## Slide 11: Cross Hair Focus
Before beginning using the instrument you must be sure that the cross-hairs are sharply focused.
Place a piece of paper in front of the telescope. Adjust the eye piece until the cross-hairs are sharply focused. Once focused the cross-hairs should remain in focus for all readings.
NOTE: If the operator changes readjust the cross-hair focus as their eye-sight may be different.

## Slide 12: Stadia Distance Measuring
Distance measuring can be done using the stadia hairs of the reticle (cross hairs). Note: This is not an accurate distance measurement.
The distance between the upper stadia hair and the lower stadia hair is usually set to 1:100 ratio.
So if the difference is 1 foot, the person holding the grade rod is 100 feet away from the instrument.