## Slide 1: Surveying Skills
Lesson 7
Rod Reading
Notes: This is foundation for other skills.

## Slide 2: Rods
Three type of rods are commonly used in agriculture:
  Builder’s or Architect’s rods – Feet and Inches
  Philadelphia rods or Engineer’s rods – Feet and 100ths of feet
  Direct Elevation Rods – Feet and 100ths of feet (commonly used with laser levels)

## Slide 3: Using the rod
The rod should always be extended to full length to insure accurate readings in each section.
The rod must be held plumb (vertical). If the rod is slanted then the reading will be greater than the actual vertical distance. Rod Levels can help the user hold it plumb.
Notes: Rod level is attached to the rod with a strap or screw. The rod is plumb when the bubble is centered.

## Slide 4: Rod Target
For longer distances it is often hard for the surveyor to directly read the rod.
A target is moved by the rodman to determine an accurate reading.
The rodman then reads and records the reading based on the position of the target.

## Slide 5: Reading the Rod Scale
Rod scales differ from tapes. With a tape you read the marks (graduations). With a rod the marks are wide and you read the edges.

## Slide 6: Numbers
The largest numbers, usually red, are whole feet.
Feet are also repeated as small numbers to aid in reading when you cannot view the whole foot.
The smaller black numbers are either inches or 10ths of feet depending on the type of rod.

## Slide 7: Markings
Note the length of the marks and the end.
Longest marks will be either 10th or inches. The point edge is the reading.
The next longest mark is ½ at the point edge. In builder’s rods this will be ½”, In Philadelphia rods this will be .05’.

## Slide 8: Graduations
Builders' rods are in feet and inches so the width of the mark and space in between is 1/8”.
For rods in feet and 100ths of feet the width of the mark and space in between is .01 feet.
Philadelphia rods and builder’s rods read like a tape measure down is zero.
Direct elevation rods read top to bottom.
Commonly even feet are written in red and inches or 10ths of feet in black letters.

## Slide 9: Builder’s Rod
What is the reading at “A”
What is the reading at “B”
What is the reading at “C”
A
B
C
Notes: A= 3’, B=2 feet 9 ½”, C=2’ 7 ¾”

## Slide 10: Philadelphia Rod
What is the reading at “A”
What is the reading at “B”
What is the reading at “C”
A
B
C
Notes: A= 6.00’, B=5.85’, C=5.63’

## Slide 11: Laser Level Receivers
Laser receivers attach to the rod and are moved up and down the rod until centered on the laser beam.
The reading is then taken at the pointer location.
Notes: What is the reading? 8’ 1 5/8”….

## Slide 12: Direct Elevation Rods
The rod has an adjustable tape.
Initially the tape is adjusted to a fixed reading at a BM.
It reads directly (or backwards) so the lower the elevation the lower the rod reading. No subtraction of the HI is required.
Tape
Tape Lock