## Slide 1: Surveying Skills
Lesson 8
Setting Grade
Notes: This is foundation for other skills.

## Slide 2: Introduction
Setting grade or “fall” is the process of using a level to set forms to a specific elevation.
Note that the actual elevation is arbitrary. We are concerned with the difference between points on the forms be a specified amount.
For level forms like a building pad (slab) the difference will be zero.
For driveways, hog pens, etc. this will usually be specified in inches per foot to allow for drainage.
Common grades might be 1/8”/ foot or ¼”/foot. For example the fall in a 16’ driveway at ¼”/foot would be: ¼”/foot x 16’ = 4”

## Slide 3: Procedure for small forms
Assume the form below is 12’x16’ and the fall will be in the direction of the arrow. The desired fall is ¼”/Foot
A
B
D
C

## Slide 4: Calculate the “fall”
16’ x ¼”/foot =4”
A
B
D
C

## Slide 5: Procedure for small forms
On the 12 foot side place two stakes on the outside of the form, near the corner (A & B), and nail or screw to the form about 6” off the ground. This will be the “top” of the slab.
Place stakes outside of form on the side opposite the first stakes (C&D).
Setup up the level instrument near the forms and adjust it to level.
Level the first (top) side. Take a measurement with the level in corner A and then a second in the corner B. Adjust the stakes until the readings are the same.
Now go to a lower corner and adjust the form on the stake until the reading is 4” (our fall) greater than the top.
Repeat with at the other lower corner.
Now double check square and all of the readings. Adjust as necessary.
Notes: This procedure is used in the activity

## Slide 6: Calculating Concrete Volume
After setting your forms you will need to order concrete.
For example if your form is 12’ x 16’ x 4” thick you would calculate: 12’ x 16’ x 4” ÷ 12”/foot = 64 cubic feet
Now convert to cubic yards to order the concrete 64 cu.ft. ÷ 27 cu.ft./cu.yd. = 2.37 cu.yd. ≈ 2.5 cu.yd.* (* we round up for ordering)
Notes: Make up a few other examples and work together.

## Slide 7: Batter Boards
Larger foundation are often set with “batter boards”.
At each corner a couple feet outside the foundation three stakes are placed.
Using a rod and instrument the stakes are marked with the finish grade level.
Horizonal “ledger boards” are attached so the top represents the finished grade. These are rechecked with an instrument.
String lines are then stretched to locate the exact grade for the forms.
For rectangular forms the diagonals are measured to ensure string lines are square.
Notes: Tie square checking in from earlier lesson. Can also be a cool activity. Do on a lawn. Screw tother batter boards so they can be re-used.

## Slide 8: Setting Grade for a Pipeline
Gravity fed pipe for irrigation or sewer are also set in the same way.
For example:
  Sewer pipes in buildings are commonly set ¼”/foot fall to insure a smooth flow of effluent.
  Irrigation pipe may be set to grades such as 1/10’ per 100’ or 3/10’ per 100 feet.
Stakes can be used (marked with grade) or the pipe can be adjusted as each section is laid.

## Slide 9: Setting Grade for Surface Drainage
For surfaces like parking lots or yards stakes are usually installed at regular intervals and marked as cut (C) or Fill (F). The elevation is measured with a rod and level at each station and the cut or fill required marked on the stake.
Cut stakes will have a distance (ex. 0.43’) from the surface to the proper cut depth. Cut stakes will be left undisturbed until the last minute so the depth of cut can be measured.
Fill stakes will have distance as well as a mark to where the new grade will be.
Marks call a crowfoot look like sideways K. Are used as a reference to measure from. The “>” in the crowfoot points in the direction of the measurement.

## Slide 10: Grade Problems
When setting forms for building foundation if one corner reads 5’ 4 3/8” what should the other corners read?
A 20’ long driveway is designed to have a ¼”/foot slope. How much fall will there be in the forms?
A sewer pipe from a hog barn to a pond is 100’ long. To maintain a grade of ¼”/foot how much fall is needed?
In the above problem the pipe elevation at the barn is 4’ 3 ½”. What should elevation be at the pond?
Notes: If the foundation is level all corners are the same!
20’ x ¼”/foot= 5”
100’ x ¼”/foot = 25” or 2’ 1”
Note: Need to ADD (lower elevation). 4’ 3 ½” + 2’ 1” = 6’ 4 ½”