## Slide 1: Surveying
Lesson #9
Differential Leveling

## Slide 2: Definition and Use
Differential leveling is the process of measuring vertical distances from a known elevation point to determine elevations of unknown points.
Common applications of differential leveling are:
  Measuring field slope for irrigation
  Measuring pipeline slope
  Grading of roads

## Slide 3: Terms
Bench Mark (BM) – A point of known (or assigned) elevation.
Backsight (BS) – A sighting or measurement to a point of known elevation (BM).
Height of the Instrument (HI) – The computed elevation of the level.
Foresight (FS) – A sighting to a point of unknown elevation.
Turning Point (TP) – A foresight that is then used for a backsight when the level is moved.

## Slide 4: Computations
Notes: Encourage students to use common sense to understand the process and not try and memorize formulas. Measure up to the level of the instrument (add) and measure down from the level of the instrument.

## Slide 5: Keeping the “book”
Measurement are recorded in columns to locate the stations and measurements.
HI and Elevations are computed.
Station | B.S. | H.I. | F.S. | Elevation
BM | 5.50 | 105.50 |  | 100.00*
1 |  |  | 4.50 | 101.00
2 |  |  | 3.50 | 102.00
3 |  |  | 4.00 | 101.50
4 |  |  | 4.50 | 101.00
5 |  |  | 5.00 | ???
*known |  |  |  | 
Notes: Station 5 = 105.50-5= 100.50

## Slide 6: Leveling Procedure
The BM elevation is known or set to an even height (ex. 100.00 feet).
Set up and level the instrument at the approximately halfway between the BM and turning point (TP).
  It is generally recommended that the distance from the instrument to the benchmark not exceed 400 feet; approximately 200 feet is the usually recommended distance.
  It is also recommended that the instrument be set up close to halfway between two benchmarks in order to cancel out leveling errors.
Send the rodman to the BM and record the rod reading. This is what is known as a backsight (BS) reading and is recorded under BS in the field notebook.
  Add the BS reading to the elevation of the BM to give the height of the instrument (HI), i.e., HI = 3.02’ + 100.00’ = 103.02’.

## Slide 7: Leveling Procedure (Cont.)
Move the rodman to next station and record this as a foresight (FS) reading in your field notebook.
  Subtract this FS reading from the HI reading to obtain the elevation at point TP-1, i.e., 103.02’ - 3.68’ = 99.34’.
Move the level instrument to the second level set-up location and set up and level the instrument.
Take another rod reading from back to the last foresight (TP). Record this backsight reading (3.34’) in the field notebook.
  Add the BS reading to the elevation of TP-1 to give the height of the instrument (HI), i.e., HI = 3.34’ + 99.34’ = 102.68’.
Repeat the process until all stations are measured.

## Slide 8: Differential Leveling Process
Notes: The activity does not move the level as the distance is small.