## Slide 1: Surveying Skills
Lesson 10
Topographic Mapping & Land Leveling

## Slide 2: What is Topography Mapping?
A map of the land showing elevations
Most commonly the map has lines of equal elevation
In differential leveling we are interested in measuring elevations along a line.
In topographic mapping we are measuring elevations in 2 dimensions.
The process of determining the station elevation remains the same.

## Slide 3: Examples
USGS Topo Map

## Slide 4: Examples (Cont.)
GPS Field Map
Notes: RTK GPS System used for leveling and other precision ag applications collect position and elevation information. This can be plotted as a topo map. Left plot is the topo. Middle is all the sample points. The inset shows the density of the sample points. On the topo plot notice “fall of the field is S-N and the “side fall” E-W.

## Slide 5: Examples (Cont.)
Google Map
Notes: Try using an interactive map in google for your area. Note: these maps are created using a DEM or digital elevation model. DEMs are available for the entire world and commonly use 30 meter grid. The are not accurate enough for survey work.

## Slide 6: Examples (Cont.)
Farmed Fields
Notes: See site in resources.

## Slide 7: Examples (Cont.)
Contours
Notes: Arrow shows slope. Note this map is west of Junction City, OR Contour Interval = 5’

## Slide 8: Uses in Agriculture
Land Leveling for Irrigation
  Typical irrigation slopes are 1-3%
  Needed for field drainage even if irrigation method is not surface like furrow or flood
Rice Checks
  In growing rice, the field is maintained with standing water.
  Checks are small ridges that hold the water and must be at a fixed elevation.

## Slide 9: Rice Checks
Leveled Field Checks are Straight
Unlevel Field Checks Follow Natural Contours
Uses in Agriculture
Notes: Rice checks follow the contour of the land to contain water.

## Slide 10: Historic Leveling Practice
Staking.
  Done on 100’ grid
  Elevations were taken with a level at each grid point.
  Cuts (where soil is removed), and fills (where soil is added) were computed for each stake
Manual Grading
  Using manually operated machinery soil was moved based on the stake marks for high spots to low points in the field.
Laser grading
  A laser transmitter was setup in the field to the grade desired.
  Earth moving equipment equipped with a laser receiver is driven around the field and the equipment automatically adjust to cut and fill.
  (photo next slide)

## Slide 11: Laser Equipment
Receiver
Transmitter
Notes: Laser equipment is being replaced by GPS, but is still commonly used. GPS is not affected by the curve of the earth (large fields) or by dust.

## Slide 12: Modern Practice
Modern leveling equipment uses Global Positioning System (GPS) receivers
First the tractor or ATV with the receiver and the GPS unit will log elevations, collecting many more data points than traditional staking.
Second using the collected data points software in the unit will create a cut/fill map.
Third the operator of the earth moving equipment then drives around the field and the GPS adjusts the implement to make the cuts and fills.
Notes: Note: These system use RTK GPS (centimeter accuracy)

## Slide 13: GPS - Equipment
GPS Receiver
Notes: Note: A GPS base station is also required. This will be located with in 6 miles of the field being leveled.

## Slide 14: GPS - Accuracy
Your phone has a GPS and is generally accurate to about 10’ 95% of the time. This is not accurate enough to survey.
Survey units use a form of GPS called Real-time Kinematic (RTK). This requires a base station located at a known point within 6 miles of the survey location.
RTK is accurate to 2 cm (95%) of the time.
RTK is used by land surveyors, land levelers, and for precision guided agricultural equipment.
Notes: 95%? This is sometimes referred to as RMS (Root mean square). Basically think of this as the reading will fall with in 2 standard deviations of the actual position. See GPS spec sheet for examples.

## Slide 15: RTK GPS Base Station
Base station is installed directly over a benchmark.
A plumb bob is used to establish this position.
The position of the benchmark is programed into the unit.
The base station then transmits a correction to the mobile unit in the field to allow for highly accurate measurements.
Notes: Not only are RTK receivers costly it requires two, the base station and mobile unit. Note: Given time a base station can establish its own location by collecting lots of readings. Uning this method a BM is not needed. However the base station cannot be moved.

## Slide 16: Cut/Fill Map
Notes: Soil is moved from red to blue

## Slide 17: Topographic Map
Notes: Line indicates the slope.

## Slide 18
Making a Topographic Map
  Layout a Grid
  Using a level determine elevations of the grid points
  Plot the grid and elevations on a map.
  Mark the locations of equal elevation on the map.
  Connect the marks of equal elevation with a line.
Topographic Map

## Slide 19
Establish the Grid
  Begin by measuring a grid in the area to be mapped. For large area this may be 100’ or less for smaller fields.
  The purpose of the grid is to be able to transfer field measurement to a map.
  Install stakes are each grid point and label rows with numbers and columns with letters (ex. C3).
  Create a map in a book or graph paper showing the grid points to scale.
Topographic Map

## Slide 20
Measure the Elevations
  Once the area is “staked”. Pick a reference point for a benchmark. Locate it on your map.
  Using differential leveling techniques determine the elevation of each grid point.
  Record these in your book (stations).
  Transfer the elevations to your map.
Topographic Map

## Slide 21
Draw the Topo Map
  Determine the elevation difference between the lines. Ex. 1 foot, 40 feet. Steeper slopes will require lines to be further apart.
  Between each survey point mark where the lines are located.
  Connect the marks of equal elevation.
  Label the lines.
Topographic Map

## Slide 22
Topographic Map - Place dots on the grid of equal elevation

## Slide 23
Topographic Map - Connect dots on the grid of equal elevation

## Slide 24
94
95
96
Topographic Map – Label the Lines

## Slide 25: Cut/Fill Calculations
If the field is staked on a regular grid like 100’x100’ then each elevation represents a fixed area. In this case 10,000 square feet.
The average elevation can be computed by averaging all the elevations.
Cut/Fill Ratio: When soil is moved it settles. When calculating the cuts and fills more soil will need to cut than filled. A typical soil might require 10-30% extra cut volume.
After applying the cut/fill ratio the average elevation of the field will be slightly less that the original.
Fortunately modern software will do the calculations required and apply the cut/fill ratio.
Notes: AZ Book has the procedure to do the math, but this really no longer needs as GPS will do the calc.

## Slide 26: Example volume calculation
Assume a station (100’ grid) needs to be cut .3’ the volume would be: 100’ x 100’ x .3’ = 3000 cubic feet Or 3000 cu. feet ÷ 27 cu. feet/cu. yard= 111 cu. yds.
Note that it does not take much of a cut to require hauling a lot of soil.