## Slide 1
Pine
A softwood used for small projects and mouldings.
Notes: Woodworking-Wood Image: pine.jpg Height: 144 Width: 106.8

## Slide 2
Pressure Treated Lumber
Generally fir species that is treated to resist decay. Green in color.
Notes: Woodworking-Wood Image: PressureTreated.jpg Height: 361 Width: 701

## Slide 3
Plywood
Composed of layers of wood sheets with the grain of each sheet glued at right angles. Very strong. Used for flooring, roof sheeting, and shear walls. Comes in various grades denoted by letters. A=best, D=worst. For example AC would be A on one side and C on the other. Plywood can be designated as interior or exterior depending on the type of glue used in its manufacture.
Notes: Woodworking-Wood Image: Plywood.jpg Height: 341 Width: 300

## Slide 4
Particle Board
Primarily made from sawdust. Used for subfloor where shear strength is not needed.
Notes: Woodworking-Wood Image: Particle.jpg Height: 213 Width: 438

## Slide 5
Oriented Strand Board (OSB)
Primarily made from wood chips. Used for shear walls and roof sheeting
Notes: Woodworking-Wood Image: wood11.jpg Height: 241 Width: 458

## Slide 6
Cedar
Known for its resistance to decay. Used for fencing.
Notes: Woodworking-Wood Image: Cedar.jpg Height: 267 Width: 447

## Slide 7
Douglass Fir
Used primarily for structural framing. Very strong.
Notes: Woodworking-Wood Image: DougFir.jpg Height: 316 Width: 266

## Slide 8
Redwood
Known for its resistance to decay. Used for landscaping, decking, etc.
Notes: Woodworking-Wood Image: Redwood.jpg Height: 332 Width: 570

## Slide 9
Oak
A hardwood used for cabinets and similar applications. The grain is very distinctive. May be used as a solid wood or as a veneer on plywood or particle board.
Notes: Woodworking-Wood Image: Oak.jpg Height: 222.6 Width: 298.2

## Slide 10
Birch
A hardwood used for cabinets, door veneer, and similar applications. May be used as a solid wood or as a veneer on plywood or particle board.
Notes: Woodworking-Wood Image: Birch.jpg Height: 72 Width: 72

## Slide 11
Tack Hammer
One side of the head is magnetic and used for starting short tacks.
Notes: Woodworking-Hammers (Wood) Image: Tack hammer.jpg Height: 86.88 Width: 240

## Slide 12
Straight Claw Hammer
The hammer head is the same as a curved claw hammer, but the claw is nearly straight. Weight 16-28 oz. Head may be smooth or serrated. Also called a Ripping hammer.
Notes: Woodworking-Hammers (Wood) Image: Straight Claw Hammer.jpg Height: 99.84 Width: 240

## Slide 13
Curved Claw Hammer
Used for driving and puling nails. Face is commonly rounded for finish work. Weight 13-16 oz.
Notes: Woodworking-Hammers (Wood) Image: CurvedClawHammer1.jpg Height: 119.52 Width: 240

## Slide 14
Mallet
Heads are made of wood, plastic, rawhide and rubber. Also called a Soft Headed Hammer.
Notes: Woodworking-Hammers (Wood) Image: Mallet.jpg Height: 117.6 Width: 240

## Slide 15
Shingler’s Hatchet
It has a gauge that can be adjusted for the desired shingle exposure and has a nail pulling slot in the back and above the cutting edge.
Notes: Woodworking-Hammers (Wood) Image: SingleHatchet.jpg Height: 39.12 Width: 72

## Slide 16
Back Saw
This saw should be used in a horizontal position.
Notes: Woodworking-Saws And Accessories Image: back saw.jpg Height: 68.64 Width: 240

## Slide 17
Hand Cross Cut Saw
The standard length is 26 inches. Typically 8-12 teeth/inch.
Notes: Woodworking-Saws And Accessories Image: hand saw.jpg Height: 63.84 Width: 240

## Slide 18
Hand Rip Saw
The edges of the teeth are not beveled, but are shaped like chisels. Typically 4-7 teeth/inch.
Notes: Woodworking-Saws And Accessories Image: hand saw.jpg Height: 63.84 Width: 240

## Slide 19
Keyhole or Compass Saw
Used for sawing curves, especially where the cut must be started from a hole bored with an auger bit.
Notes: Woodworking-Saws And Accessories Image: compass saw.jpg Height: 65.28 Width: 240

## Slide 20
Coping Saw
The blade is installed to cut on the pull stroke.
Notes: Woodworking-Saws And Accessories Image: coping saw.jpg Height: 113.28 Width: 240

## Slide 21
Belt Sander
Sands or cuts using a sanding belt. Used for course sanding of large surfaces.
Notes: Woodworking-Power Tools Image: Belt Sander.jpg Height: 300 Width: 300

## Slide 22
Jack Plane
Planing should be done with the grain of the wood. Note tail behind the handle.
Notes: Woodworking-Planes And Similar Tools Image: Jack plane.jpg Height: 107.04 Width: 240

## Slide 23
Circular Saw
Primarily used for cutting wood, however many blades types are available for cutting sheet metal, metal, stone, and various other products. Available as a direct drive or worm drive.
Notes: Woodworking-Power Tools Image: power7.jpg Height: 321 Width: 400

## Slide 24
Smooth Plane
Sizes range from 5 1/2 to 10 inches long and 1 1/4 to 2 3/8 inches wide.
Notes: Woodworking-Planes And Similar Tools Image: Smoothing Plane.jpg Height: 214.8 Width: 271.8

## Slide 25
Finishing Sander
Sands by a vibrating action.
Notes: Woodworking-Power Tools Image: Palm Sander.jpg Height: 300 Width: 300

## Slide 26
Block Plane
Sizes range form 5 1/2 to 7 inches long and 1 3/8 to 1 5/8 inches wide. Used to plane the end of a board.
Notes: Woodworking-Planes And Similar Tools Image: block plane.jpg Height: 97.44 Width: 240

## Slide 27
Router
Depth of cut is adjustable. Used to shape wood (ex. round the edge of a board).
Notes: Woodworking-Power Tools Image: Router.jpg Height: 300 Width: 300

## Slide 28
Circular Saw Blade
The size is determined by the diameter of the blade.
Notes: Woodworking-Power Tools Image: Circular Saw Blade.jpg Height: 300 Width: 300

## Slide 29
Jig Saw
Many variations of blades are available for cutting wood, plastics, and other soft materials. Also called a Saber Saw
Notes: Woodworking-Power Tools Image: Jig Saw.jpg Height: 300 Width: 300

## Slide 30
Power Miter Saw
The saw pivots on the miter box for various angles.
Notes: Woodworking-Power Tools Image: spower3.jpg Height: 252.6 Width: 309

## Slide 31
Nail Gun
Nails are fed automatically from a loading chamber and are dispensed by pulling the trigger.
Notes: Woodworking-Power Tools Image: Nailer.jpg Height: 500 Width: 500

## Slide 32
Planer
Used for planing wood surfaces. A portable power version of a hand plane.
Notes: Woodworking-Power Tools Image: Planer.jpg Height: 300 Width: 300

## Slide 33
Reciprocating Saw
Similar to the jig saw but much larger and used for heavy duty work.
Notes: Woodworking-Power Tools Image: RecipSaw.jpg Height: 300 Width: 300

## Slide 34
Disc Sander
A stationary power tool with a 6-12 inch sanding disc.
Notes: Woodworking-Power Tools Image: DiscSander.jpg Height: 198 Width: 240

## Slide 35
Forstner Bit
A power bit for drilling flat bottomed holes in wood. Commonly found in sizes 3/8-2 inch.
Notes: Woodworking-Boring Tools (Wood) Image: Forstner.jpg Height: 345 Width: 349.8

## Slide 36
Hole Saw
Hole saws come in sizes from ¾ to 2 1/2 inches and one mandrel fits all.
Notes: Woodworking-Boring Tools (Wood) Image: HoleSaw.jpg Height: 320 Width: 320

## Slide 37
Auger Bit
The straight round shank adapted for power drills.
Notes: Woodworking-Boring Tools (Wood) Image: AugerBit.jpg Height: 192 Width: 192

## Slide 38
Spade Bit
A wood boring bit with a hex shaft to be used in a power hand drill or drill press.
Notes: Woodworking-Boring Tools (Wood) Image: SpadeBit.jpg Height: 300 Width: 300

## Slide 39
Expansive Bit
The shank is a square taper, adapted for the bit brace.
Notes: Woodworking-Boring Tools (Wood) Image: ExpansiveBit.jpg Height: 96 Width: 96

## Slide 40
Surform Tool
A tool like a wood rasp with a replaceable cutter. Available in flat, round, and half round shapes.
Notes: Woodworking-Woodworking Tools Image: surform tool.jpg Height: 103.2 Width: 240

## Slide 41
Nail Set
The point has a slight hollow at the end.
Notes: Woodworking-Woodworking Tools Image: NailSet.jpg Height: 41.76 Width: 240

## Slide 42
Hand Screw Clamp
The wooden handles are mounted on opposite sides of the jaws.
Notes: Woodworking-Woodworking Tools Image: clamp6.jpg Height: 1000 Width: 1000

## Slide 43
Cat's Paw
A tool used to pull nails
Notes: Woodworking-Woodworking Tools Image: CatsPaw.jpg Height: 172.2 Width: 579

## Slide 44
Wood Chisel
It is sharpened only on one side to a 25 or 30 degree angle and may be used with or across the grain.
Notes: Woodworking-Woodworking Tools Image: Wood Chisel.bmp Height: 300 Width: 300

## Slide 45
Wood Rasp
Other rasps are 4-in-hand and horse rasps.
Notes: Woodworking-Woodworking Tools Image: WoodRasp.jpg Height: 288 Width: 384

## Slide 46
Nail Puller
A pair of jaws is driven into the wood below the nail head by impact action of the handle.
Notes: Woodworking-Woodworking Tools Image: NailPuller.jpg Height: 393.75 Width: 525

## Slide 47
Utility Knife
A sharp knife for cutting drywall, roofing felt, etc.
Notes: Woodworking-Construction Image: UtilityKnife.jpg Height: 86.88 Width: 240

## Slide 48
Drywall Trowel
A flexible trowel for applying drywall compound and tapping.
Notes: Woodworking-Construction Image: Drywall taping knife.jpg Height: 205.92 Width: 240

## Slide 49
Drywall Saw
A tapered hand saw for cutting drywall.
Notes: Woodworking-Construction Image: drywall saw.jpg Height: 35.52 Width: 240

## Slide 50
Drill Press
A stationary drill.
Notes: Woodworking-Stationary Power Tools Image: Drill Press.jpg Height: 353.76 Width: 180

## Slide 51
Band Saw
Used for making curved cuts in wood or metal.
Notes: Woodworking-Stationary Power Tools Image: Bandsaw.jpg Height: 353.52 Width: 180

## Slide 52
Radial Arm Saw
A saw designed to cross cut and rip with the ability to cut compound angles.
Notes: Woodworking-Stationary Power Tools Image: radialArm.jpg Height: 400 Width: 309

## Slide 53
Table Saw
A stationary saw used primarily for ripping lumber and sheet materials.
Notes: Woodworking-Stationary Power Tools Image: Table Saw.jpg Height: 180 Width: 263.04