## Slide 1: 6 x 10 Shed Construction Photos
California Agricultural Education

## Slide 2
Mark cut line with an “X” on the kerf side of the line

## Slide 3
Pair plates and joists, mark stud and joist locations

## Slide 4
Use a square to mark both plates so they will match

## Slide 5
Installing floor sleepers with screws

## Slide 6
Floor joist installation

## Slide 7
Check square by measuring diagonals

## Slide 8
Tacking plywood sub floor

## Slide 9
Trimming sub floor in place

## Slide 10
DSC_0513

## Slide 11
Plates marled before assembly

## Slide 12
2x4 should be nailed with two nails per stud.

## Slide 13
Mark trimmers and cripples

## Slide 14
Window framing

## Slide 15
Trimmer installation

## Slide 16
Trimmer and header installation

## Slide 17
Marking joist nailing locations with a chalk line

## Slide 18
DSC_0518

## Slide 19
Nailing trimmers to studs at an angle so nails will not poke through

## Slide 20
Nailing 4x4 header

## Slide 21
DSC_0527

## Slide 22
Cutting door opening (used to make door)

## Slide 23
Checking wall framing for square

## Slide 24
DSC_0531

## Slide 25
Setting a wall with a temporary brace

## Slide 26
Using a jig on the miter saw to cut rafter tails

## Slide 27
Jig

## Slide 28
Using the jig to create truss

## Slide 29
OSB collar tie is installed with glue and screws, mark glue location

## Slide 30
Add glue

## Slide 31
Screw in collar tie

## Slide 32
Finished truss

## Slide 33
Door assembled with glue and screws

## Slide 34
One screw from each side

## Slide 35
Finished exterior frame

## Slide 36
Installation of interior framing

## Slide 37
Trim plywood edge flush

## Slide 38
Install walls with screws or nails

## Slide 39
Mark truss locations on top plate

## Slide 40
Install gable end trusses with ridge board, then add interior trusses

## Slide 41
Connection to ridge board

## Slide 42
Use screws or nails

## Slide 43
Install heel cut end with screws or nails

## Slide 44
Installing trusses

## Slide 45
Installed trusses

## Slide 46
Walls and trusses installed

## Slide 47
Trusses

## Slide 48
Osb installed on trusses, gable end siding installed

## Slide 49
Window installation with screws

## Slide 50
Two methods of installing shelves

## Slide 51
Wood shelf brace

## Slide 52
Shelf support

## Slide 53
Installed shelves

## Slide 54
Corner trim

## Slide 55
DSC_0573

## Slide 56
Window trim

## Slide 57
Door Trim

## Slide 58
Scrap trim for door stop

## Slide 59
Finished door

## Slide 60
Trimmed rear side

## Slide 61
Trimmed front side

## Slide 62
Trimmed end

## Slide 63
Never leave tools on a ladder!

## Slide 64
Minimal waste