## Slide 1: Garden Sheds

## Slide 2: Agenda
Overview
  Next level – good example to teach construction skills
  Includes layout skills – transferable to other projects
  Orientation to plans
Tools
Learning Outcomes
Cutting Lists
Bills of Materials
Construction Tips
Customize the Shed
Resources

## Slide 3: Quiz Key
What is a sinker? A vinyl cement coated nail.
A roof slope is described as 4/12 meaning it rises 4” for every 12” of run .
The actual size of 2” x 4” surfaced lumber is: 1 ½” x 3 ½”.
A rafter supports the roof of the building.
A 2”x6”x12’ board contains 12 board feet.
Lumber used for framing commonly comes from fir, hemlock, or spruce trees.
The horizontal framing member at the top of a wall is called a plate.
Galvanized coating on nails is used to prevent rusting.
The material used under composition shingles is called roofing felt or tar paper.
OSB or plywood is commonly used as sheeting to cover walls or the roof framing.

## Slide 4: Activity #1 - What Tools Are Required? Make your list – required/optional
Required
Steel Tape
Framing Square
Circular Saw
Hammer
Utility Knife
Screwdriver
Optional
Power Miter Saw
Hammer Tacker
Cat’s Paw
Power screw driver
Level
And ….

## Slide 5: Building Process
Plans & drawings
Cutting Lists
And
Bill of Materials
Knowledge
Of Materials
Layout
Plan reading
Measuring
Construction
Tool selection & use
Construction Methods

## Slide 6: Activity #2 Student Learning Outcomes
Review the plan. What SLOs will students learn by completing the project?
10 min & share

## Slide 7: Student Learning Outcomes
Students will:
Read and interpret plans common to wood framed buildings
Identify common parts of a building by name (e.g.; header, cripple)
Create a cut list using the plans
Create a bill of materials and estimate the cost of the building
Identify common fasteners and materials used in wood frame construction
Identify common tools used in wood frame construction
Cut lumber based on a cut list
Layout floor joists
Build a framed floor with joists and sheeting
Square a framed floor or wall section

## Slide 8: Student Learning Outcomes
Layout wall plates
Assemble a wall with window and door openings
Cut and apply siding to a wall
Install windows
Determine the roof angle and layout with a square
Cut a rafter
Layout rafter locations
Frame a roof
Cut and apply roof sheeting
Install a roofing system such as composition roofing of steel.
Cut and install trim

## Slide 10
Cripple
Header
Stud
Trimmer
Plate

## Slide 11: Activity #2
Create a cutting list for the walls using the plan
15 minutes
Common lumber sizes: 2x4x8’, 2x4x10’, 2x4x12’, 2x4x14’, 2x4x16’
No siding or window. Framing Only

## Slide 12: Review cut list and process
Qty | Material | Dimension(s) | Notes
12 | #2 or BTR S4S Fir | 2x4x86 3/4" | Studs
4 | #2 or BTR S4S Fir | 2x4x120" | Plate
2 | #2 or BTR S4S Fir | 2x4x113" | Plate
1 | #2 or BTR S4S Fir | 4x4x27" | Window Header
1 | #2 or BTR S4S Fir | 4x4x41 1/2" | Door Header
1 | #2 or BTR S4S Fir | 2x4x27" | Sill
1 | #2 or BTR S4S Fir | 2x4x56 3/4" | Cripple
2 | #2 or BTR S4S Fir | 2x4x56 3/4" | Window Trimmer
2 | #2 or BTR S4S Fir | 2x4x81" | Door Trimmer
2 | #2 or BTR S4S Fir | 2x4x24" | Window Trimmer

## Slide 13: Review the Process for Bill of Materials
Layout is important
Utilization
Standard sizes
Combine similar materials
Use published prices

## Slide 14: Activity #3
Create a bill of materials based on the cut list.
20 minutes
(need handout form and pricelist)
(Make a key)

## Slide 15: BOM Key
How close did you get?
Material | Units | Qty | Price | Total |  | Notes
2x4x8 | ea | 17 | 2.75 | 46.75 |  | Studs, door trimmers, cripple
2x4x10 | ea | 6 | 3.64 | 21.84 |  | Plates, window trimmer
4x4x8 | ea | 1 | 8.55 | 8.55 |  | Window trimmer, sill
 |  |  | TOTAL | 77.14 |  | Header

## Slide 16: Uses/Materials
SAE – student or a small team can build and sell
Class project – Custom build
Team building activity
Lumber yards vs. Home Improvement Stores
Contractor's discounts

## Slide 17: Team building activity
Pre-cut lumber
Bundle by use (floors, walls)
Mark layout

## Slide 18: Tips
Use jigs when possible
Check square multiple times
Install siding flat
On some designs you can build roof on the ground. Think ahead on the attachment.
Look for ways to conserve materials.
Layout plates/joists in pairs. Check before assembly

## Slide 19: Transportation
Build complete or in flat sections
Use “peelers” as rollers
Tiltbed trailers are useful

## Slide 20: Transportation
Build complete or in flat sections

## Slide 21: Customizations
Changing the design
Trim options
Roof – metal or comp
Shelves
Workbench
Wiring – note likely a code violation use caution

## Slide 22: Resources
www.agedweb.org/sheds
Books
CAD
  AutoCAD educational version
  Free 2D programs